## Slide 1
Case Studies

## Slide 2
Climate Hazards and Impacts

## Slide 3: Case Study: Inundation and Flooding Maps Capital Regional District (Victoria, BC)
High Tide + 0.5m SLR (2050)
Storm Surge + 0.5m SLR (2050)
Storm Surge + 1.0m SLR (2100)
Storm Surge + 2.0m SLR (2200)
Notes: Climate Change Hazard and Impacts Case Study – Victoria, BC, Canada [1/4]
Speaker Notes:
Victoria Capital Regional District
SLR vulnerability and economic analysis
The primary purpose of this study was to map SLR and storm inundation and identify areas that are vulnerable within the CRD. 6 total scenarios were evaluated for the area: 3 using high tide as the reference water level, and 3 using a 500-year storm surge, all using sea level rise expected for 2050, 2100, and 2200. The 6 scenarios were mapped regionally and the study examined 24 focus areas in detail. This is the focus of this slide.
The secondary purpose was to understand the potential economic consequences of SLR to support development of future policy and land use regulations through development of three case studies which looked at transportation disruption (based on disruption to Highway 14 south of Shirley), local community disruption (in the Oak Bay Windsor Park residential area), and business disruption (in the Victoria Inner Harbour). This detail is on another slide shown later under risk assessment.
-----------------------------------------------------------------------------------------------
CASE STUDY
Capital Regional District Coastal Sea Level Rise Risk Assessment
Stressors covered: Sea level rise and coastal flooding; Time Horizons: 2050, 2100, 2200
Project components: Climate change scenarios; Asset prioritization (including stakeholder workshops); SLR mapping; case studies on business, transportation and community economic/financial impacts. .
Location: Capital Regional District (CRD), Victoria, British Columbia, Canada
Overview: The primary purpose of this study was to map SLR and storm inundation and identify areas that are vulnerable within the CRD. The secondary purpose was to understand the potential economic consequences of SLR to support development of future policy and land use regulations through development of three case studies looking at transportation disruption (based on disruption to Highway 14 south of Shirley), local community disruption (in the Oak Bay Windsor Park residential area), and business disruption (in the Victoria Inner Harbour).
Mapping scenarios considered static SLR (0.5, 1.0, and 1.5 meters) coupled with a 1 in 500 year storm surge condition to show the anticipated future shoreline at high tide and during storm conditions for the years 2050, 2100, and 2200.
Project Funding: Capital Regional District
Weblink: https://www.crd.bc.ca/docs/default-source/climate-action-pdf/coastal-sea-level-rise-risk-assessment-report.pdf

## Slide 4: Case Study: City of Baltimore Disaster Preparedness and Planning Project
Natural Hazards (including Climate Hazards) identified in Baltimore’s Hazard Mitigation Plan
Flooding (flooding and dam failure)
Coastal Hazards (tropical storms, hurricanes, sea level rise, storm surge, tsunami)
Precipitation (thunderstorms, winter storms, nor’easters, drought, hail)
Wind (storms, derechos, tornados)
Extreme Heat (heat and air quality)
Land (earthquake, landslides, sinkholes
Notes: Climate Change Hazard and Impacts Case Study – Baltimore Maryland
Speaker Notes:
Case study of asset vulnerability exercise with minimal data availability.
City of Baltimore Disaster Preparedness and Planning Project (Dp3).
Dp3 was created as a manner to address existing hazards while simultaneously preparing for those predicted by climate change. Hazards were identified as flooding, coastal hazards, precipitation, wind, extreme heat, and land movement. A 42 member Advisory Committee and several working groups focused on four key sectors that could face damage from hazards: infrastructure, buildings, natural systems, and public services. An asset inventory was performed to identify particular assets that are likely to be impacted. Adaptation strategies were created for each asset type to ensure preparedness for future natural hazards.
The only asset data provided was location
More information on the plan can be found here: http://www.baltimoresustainability.org/plans/disaster-preparedness-plan/

## Slide 5
Review Climate Science and Projections

## Slide 6: Berkeley Watershed Modelling and Climate Change
Current Watershed Masterplan evaluates performance of existing stormwater infrastructure under current conditions
New Scope of Work (SOW) developed to provide approach for incorporating climate-change-driven changes in precipitation and sea level rise into the watershed modeling.
SOW will support City investments in stormwater system upgrades and green infrastructure to achieve a higher degree of system reliability and resilience.
SOW identifies boundary condition data and scenarios for existing and future Bay water levels and precipitation events.
Notes: Climate Change Science and Projections Case Study – Berkeley, California [1/3]
Speaker Notes:
Here is a an example in which future climate conditions were developed and modeled to obtain future climate impacts on stormwater infrastructure.
Currently the Berkeley watershed masterplan evaluates the performance of stormwater infrastructure under current conditions. This project provided an approach for incorporating changes to precipitation and SLR in the watershed modeling as a way to model future conditions.
This project will help guide the city’s investments in stormwater system upgrades green infrastructure implementation
Case study example of how to use downscaled Global Circulation Model (GCM) precipitation data to develop future conditions hydrology and Intensity-Duration-Frequency (IDF) curves. IDF curves are precipitation design curves that provide information on how much rain falls (intensity) in a given period of time (duration) and how often that event occurs (frequency).

## Slide 7: Berkeley Watershed Modelling and Climate Change
Notes: Climate Change Science and Projections Case Study – Berkeley, California cont. [1/2]
Speaker Notes:
Case study example of how to use downscaled Global Circulation Model (GCM) precipitation data to develop future conditions hydrology and Intensity-Duration-Frequency (IDF) curves. IDF curves are precipitation design curves that provide information on how much rain falls (intensity) in a given period of time (duration) and how often that event occurs (frequency).
The project involved identifying future conditions hydrology and selecting climate change scenarios for Bay water levels and precipitation events.
Precipitation data were obtain from readily available GCM data output; however, these datasets are very coarse, so they had to be downscaled to represent the local Berkeley area. Once this was done, future conditions hydrology and IDF curves were developed.
The idea was that the future conditions hydrology scenarios and IDF curves would be boundary conditions to a watershed model, which would result in an analysis and evaluation of stormwater infrastructure of future conditions.

## Slide 8: Berkeley Watershed Model
Notes: Climate Change Science and Projections Case Study – Berkeley, California cont. [2/2]
Speaker Notes:
This is an example of how an IDF curve was modified (using GCM data) to represent future conditions precipitation events. An IDF curve represents Intensity-Duration-Frequency of rainfall events – essentially how much rain falls in what amount of time and how often that occurs.
For example, under existing conditions, the 10-year 3-hour precipitation amount is approximately 1.1 inches. Based on the GCM output and analysis, the 10-year 3-hour precipitation amount is projected to increase from approximately 1.1 inches to approximately 1.4 inches by 2100.

## Slide 9: Baltimore Preparedness & Resiliency Disaster Preparedness Project & Plan
-
Expand use of climate information in water resources planning and management
Research and monitor trends in storm events and stream flow
Update flood maps to reflect changing risk associated with climate change
Continuously improve and enhance flood vulnerability data
Recommendation on conducting analysis of trends in storm events and hydrology to inform climate change response policies
Notes: Climate Change Science and Projections Case Study – Baltimore, Maryland
Speaker Notes:
The Baltimore 2013 Disaster Preparedness and Planning Project Plan developed a unified approach to hazard mitigation and climate adaptation. The Federal Emergency Management Agency (FEMA) requires every local jurisdiction to adopt an All Hazards Mitigation Plan (AHMP). The Plan was created as a method to address existing hazards while simultaneously preparing for those predicted by climate change. One of the goals of the plan is to Enhance the City of Baltimore’s adaptive capacity and build institutional structures that can cope with future conditions that are beyond past experience. This slide articulates one of the actions to conduct detailed ongoing analysis of climate information, trends in storm events and hydrology to support policy changes responding to climate change. This action recommends that climate information is used in future water resources planning, flood map updates and recommends actions to continually learn from current storm events and flood events.
More information on the plan can be found here: http://www.baltimoresustainability.org/plans/disaster-preparedness-plan/

## Slide 10
Asset and Operations Inventory

## Slide 11: Case Study: Robust Asset Data Adapting to Rising Tides (ART)
Asset Data Collection Process
Initial asset data collection was mostly done using geographic information system (GIS) datasets
To reduce no. of assets for which data was collected;
Asset locations were compared with SLR hazard zones
Critical assets were identified (from functionality, use etc.)
Detailed asset sensitivity information collected following the selection of representative assets
Don’t wait for perfect data!
Notes: Asset and Operations Inventory Case Study – Bay Area, California [1/2]
Speaker Notes:
Adapting to Rising Tides Project, San Francisco Bay, CA.
This is an example of a vulnerability and risk assessment with robust data availability.
Various core transportation assets including highways, tunnels, toll plazas, bridges, etc. and adjacent assets such as parkland, recreational/commercial buildings, train stations, etc. were included in the initial list based on suggestions made by partner agencies participating in this project, including BART, Caltrans, MTC, and BCDC.
Initially, SLR hazard zones were identified and used to assist in the pre-selection of assets, then data about the functionality and other characteristics of these assets were obtained. Following that, asset sensitivity information was collected to complete the vulnerability and risk assessment
____________________________________________________________________
Name of Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area: Pilot Project
Author: San Francisco Bay Area Metropolitan Transportation Commission
Type of Resource: Pilot study report
Why read this document? For details on carrying out sea level rise assessments, use of shoreline overtopping analysis to identify areas for focused study; how to assess the sources, mechanisms, and timing of inland inundation and flooding; how to develop evaluation criteria to choose qualitatively between different adaptation strategies; details on living levees as an adaptation strategy; and how to mainstream climate change into an agency’s function
Topics covered: Sea level rise mapping, vulnerability assessment, evaluation criteria development, adaptation strategy development
Sector: Transportation
Stressors covered: Sea level rise and storm surge
Highlighted sections: The Executive Summary provides a good overview of the whole study. Chapters 5 and 6 outline design of living levees as adaptation strategies; Chapter 8 outlines how to mainstream climate adaptation into transportation agencies. Appendix B provides technical details on work carried out to identify the key areas of vulnerability that exist within three focus areas and assess the sources, mechanisms, and timing of inland inundation and flooding to inform the development of adaptation strategies.
Weblink: http://mtc.ca.gov/tools-and-resources/digital-library/climate-change-and-extreme-weather-adaptation-options
CAKE Link: http://www.cakex.org/directory/organizations/metropolitan-transportation-commission

## Slide 12: ART Project – Asset Data Collected
Examples of Assets identified in the Bay Bridge Touchdown Focus Area | 
Core Assets | Asset components
I-80/I-580 segments from Powell Street to the Bay Bridge Toll Plaza | Bay Bridge Toll Plaza Temescal Creek Bridge Tributary Drainage Areas
I-880 segment from 7th Street to the Bay Bridge Toll Plaza | Tributary Drainage Areas
East end of Bay Area Rapid Transit Transbay Tube and Track Portal (connecting Oakland to San Francisco) | Not Applicable
Adjacent Assets | Asset components
East Bay Municipal Utility District Wastewater Treatment Plant | Not Applicable
Burma Road Port Operations and Electrical Substation | Not Applicable
East shore State Park / Emeryville Crescent | Not Applicable
Notes: Asset and Operations Inventory Case Study – Bay Area, California cont. [2/2]
Speaker Notes:
The assets shown in this slide are from the Bay Bridge Focus Area (one of the 5 focus areas in the MTC Adapting to Rising Tides Project), an area on the eastern side of the Bay Bridge in Oakland. This area includes a mix of core assets such as highway segments and the Transbay tube and track portal for the train that connects San Francisco to Oakland by cutting across the Bay.
The adjacent assets include a wastewater treatment plant, an electric substation, and parkland.
All of these assets are affected by sea level rise and coastal storm surge.
______________________________________________________________________
Name of Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area: Pilot Project
Author: San Francisco Bay Area Metropolitan Transportation Commission
Type of Resource: Pilot study report
Why read this document? For details on carrying out sea level rise assessments, use of shoreline overtopping analysis to identify areas for focused study; how to assess the sources, mechanisms, and timing of inland inundation and flooding; how to develop evaluation criteria to choose qualitatively between different adaptation strategies; details on living levees as an adaptation strategy; and how to mainstream climate change into an agency’s function
Topics covered: Sea level rise mapping, vulnerability assessment, evaluation criteria development, adaptation strategy development
Sector: Transportation
Stressors covered: Sea level rise and storm surge
Highlighted sections: The Executive Summary provides a good overview of the whole study. Chapters 5 and 6 outline design of living levees as adaptation strategies; Chapter 8 outlines how to mainstream climate adaptation into transportation agencies. Appendix B provides technical details on work carried out to identify the key areas of vulnerability that exist within three focus areas and assess the sources, mechanisms, and timing of inland inundation and flooding to inform the development of adaptation strategies.
Weblink: http://mtc.ca.gov/tools-and-resources/digital-library/climate-change-and-extreme-weather-adaptation-options
CAKE Link: http://www.cakex.org/directory/organizations/metropolitan-transportation-commission

## Slide 13: Case Study: Inundation and Flooding Maps Capital Regional District (Victoria, BC)
Evaluated asset categories:
Residential
Commercial
Civic, Institutional, and Recreation
Mining, Transportation, Communications, and Utilities
Industrial
Farm
Forest
Focus Areas
Inundation Mapping
Focus Areas
Notes: Capital Regional District Coastal Sea Level Rise Asset Assessment, Victoria, British Columbia [cont] [2/5]
Speaker Notes:
Once maps were developed for the entire CRD coastline a workshop was run with the CRD Project Team to identify the key assets (e.g. key municipal infrastructure) that exist within the coastal areas that could be subject to flooding for the scenarios considered. This was used to help define SLR Focus Areas for a selection of areas with key assets and relatively high levels of expected future inundation.
-----------------------------------------------------------------------------------------------
CASE STUDY
Capital Regional District Coastal Sea Level Rise Risk Assessment
Stressors covered: Sea level rise and coastal flooding; Time Horizons: 2050, 2100, 2200
Project components: Climate change scenarios; Asset prioritization (including stakeholder workshops); SLR mapping; case studies on business, transportation and community economic/financial impacts. .
Location: Capital Regional District (CRD), Victoria, British Columbia, Canada
Overview: The primary purpose of this study was to map SLR and storm inundation and identify areas that are vulnerable within the CRD. The secondary purpose was to understand the potential economic consequences of SLR to support development of future policy and land use regulations through development of three case studies looking at transportation disruption (based on disruption to Highway 14 south of Shirley), local community disruption (in the Oak Bay Windsor Park residential area), and business disruption (in the Victoria Inner Harbour).
Mapping scenarios considered static SLR (0.5, 1.0, and 1.5 meters) coupled with a 1 in 500 year storm surge condition to show the anticipated future shoreline at high tide and during storm conditions for the years 2050, 2100, and 2200.
Project Funding: Capital Regional District
Weblink: https://www.crd.bc.ca/docs/default-source/climate-action-pdf/coastal-sea-level-rise-risk-assessment-report.pdf

## Slide 14: FHWA Post Sandy Study Images of Example Assets Assessed
Cambridge Systematics, AECOM, Abt (Stratus Consulting), Office of Radley Horton, C2E
Impacts of Climate Stressors on 10 Transportation Assets Evaluated
  6 in New York, 3 in New Jersey, 1 in Connecticut
  A mix of bridges, highways, a port, and a railroad track
Notes: Asset and Operations Inventory Case Study – New York, New Jersey, Connecticut
Speaker Notes:
Case study of Federal Highway Administration Study post-Hurricane Sandy to examine climate change vulnerability of transportation assets in the Tri-State Area (New York, New Jersey, and Connecticut).
An adaptation engineering assessment process was developed for transportation assets. To test the methodology, 10 assets were selected in 3 states that had suffered from one of the recent, major storms in the North East (such as Sandy, Irene etc.). A vulnerability assessment was carried out of the asset and adaptation solutions developed for each asset assuming a certain future climate change scenario (depending on the current age / future lifespan of the asset) rather than current day conditions.
A mix of different assets were selected including bascule bridges, highway, a port and section of railroad track. Climate Change stressors covered including SLR, precipitation, and extreme heat. Strategies included physical modifications and updating of regulatory guidelines.
10 Transportation Assets
  6 in New York, 3 in New Jersey, 1 in Connecticut
  A mix of bridges, highways, a port, and a railroad track
Range of Climate Stressors Covered
  Sea level Rise and Storm Surge (7 assessments)
  Extreme Precipitation (2 assessments)
  Extreme Heat (1 assessment)
Vulnerability Assessment included:
  Exposure, sensitivity, adaptive capacity
  Economic consequence analysis
Range of Adaptation Strategies Proposed
  Physical modifications (e.g., installation of seawalls)
  Updating regulatory guidelines (e.g., updates to zero thermal stress temperature, updates to IDF Curve)

## Slide 15
Assess Exposure

## Slide 16: Climate Change and Extreme Weather Adaptation Options
Combined Riverine and Coastal Flooding Exposure Analysis of the Coliseum Focus Area, Oakland, CA
A mix of impacted assets such as roadways, transit stations, and commercial/recreational building assets
8 combinations of Bay water levels, sea level rise, and riverine peak flows
Bay water levels: MHHW, 10-year tide, 100-year tide
Sea level rise: 24 inches
Riverine peak flows: 10-year peak flow, 100-year peak flow
Notes: Exposure Case Study – Bay Area, California
Speaker Notes:
This climate change vulnerability assessment and adaptation strategy development study focused on transportation infrastructure in the SF Bay area.
6 SLR scenarios were developed and mapped. Focus areas were identified and further analysis was conducted to develop conceptual physical adaptation strategies.
The adaptation strategies were then sorted and ranked based on a multi-criteria analysis to select 5 strategies for further conceptual design development.
The focus of this slide and the next 4 map slides are on a combined hydraulic modeling of a tidal creek with fluvial discharge and sea level rise to examine combined flooding.
__________________________________________________
Name of Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area: Pilot Project
Author: San Francisco Bay Area Metropolitan Transportation Commission
Type of Resource: Pilot study report
Why read this document? For details on carrying out sea level rise assessments, use of shoreline overtopping analysis to identify areas for focused study; how to assess the sources, mechanisms, and timing of inland inundation and flooding; how to develop evaluation criteria to choose qualitatively between different adaptation strategies; details on living levees as an adaptation strategy; and how to mainstream climate change into an agency’s function
Topics covered: Sea level rise mapping, vulnerability assessment, evaluation criteria development, adaptation strategy development
Sector: Transportation
Stressors covered: Sea level rise and storm surge
Highlighted sections: The Executive Summary provides a good overview of the whole study. Chapters 5 and 6 outline design of living levees as adaptation strategies; Chapter 8 outlines how to mainstream climate adaptation into transportation agencies. Appendix B provides technical details on work carried out to identify the key areas of vulnerability that exist within three focus areas and assess the sources, mechanisms, and timing of inland inundation and flooding to inform the development of adaptation strategies.
Weblink: http://mtc.ca.gov/tools-and-resources/digital-library/climate-change-and-extreme-weather-adaptation-options
CAKE Link: http://www.cakex.org/directory/organizations/metropolitan-transportation-commission

## Slide 17
Notes: Exposure Case Study – Bay Area, California cont.
Speaker Notes:
Here are the results of the combined riverine and coastal water level analysis. The light blue represents present-day inundation and the dark blue represents inundation that would occur with the same coastal water level and river discharge with 24’’ of SLR.
Several combinations of riverine-coastal water levels were analyzed to determine flooding pathways and vulnerable areas
This example shows inundation during a MHHW tide with a 100-yr flow.

## Slide 18
Notes: Exposure Case Study – Bay Area, California cont.
Speaker Notes:
This example shows inundation during a 10-yr tide with a 10-yr flow.

## Slide 19
Notes: Exposure Case Study – Bay Area, California cont.
Speaker Notes:
This example shows inundation during a 10-yr tide with a 100-yr flow.

## Slide 20
Notes: Speaker Notes:
This example shows inundation during a 100-yr tide with a 10-yr flow.

## Slide 21
Assess Vulnerability

## Slide 22: California State Route 37 – North San Francisco Bay Sea Level Rise Vulnerability Study and Adaptation
HWY Vulnerability Assessment conducted for each reach by examining exposure, sensitivity, and adaptive capacity.
Exposure: function of depth and extent of inundation, length of overtopped reach, and physical condition of shoreline protection features.
Sensitivity: function of reach age, level of use, historical performance during storm events, seismic and liquefaction susceptibility
Adaptive capacity: function of alternative viable route availability
Qualitative ratings assigned to each component to develop composite vulnerability rating
Notes: Vulnerability Case Study – State Route 37, California
Speaker Notes:
Case study of sea level rise vulnerability and risk assessment for state highway in North San Francisco Bay. Project included SLR inundation mapping and shoreline vulnerability assessment, conceptual engineering design and costs for alternatives, and 3-D renderings of proposed solutions.
HWY37, which runs along North SF Bay is vulnerable to the effects of SLR.
SLR inundation maps were used to determine which sections of the HWY are vulnerable to the effects of SLR. The HWY was separated into reaches and a shoreline vulnerability assessment was conducted for each reach. Using that information, adaptation alternatives were developed, which involved conceptual engineering design and cost estimates for three physical alternative to raise the elevation of the road.
Conceptual rendering of the alternative were also developed – see later slides under the adaptation solutions section.

## Slide 23
Assess Risk

## Slide 24: Case Study: Coastal Sea Level Rise Risk Assessment Capital Regional District (Victoria, BC)
Indicator | Impact
Commute Costs per day | $7,059
Emergency Services Cost per day | $441
Residential Utility Disruption Cost per day | $2,479
Recreation Cost per day | $101,951
Total Daily Impacts | $111,930
Focus Area Population | 1,388
Property Tax Revenues at Risk | $1,567,480
Focus Area
Notes: Sea Level Rise Risk Assessment- Victoria, BC [cont.] [3/4]
This is a continuation of the Victoria, BC case study.
Speaker Notes:
Once the focus areas were selected, the following data was compiled and defined:
- land use
- shoreline sensitivity to sea level rise
- valuation of land and improvements
- roads and presence of key public assets within the areas that would be flooded
This data was provided by CRD and also included
- municipal zoning data
- BC Assessment data for actual use of land and market valuation of land and improvements
- location of roads
- replacement cost estimates for key public assets.
For this Community services disruption case study :. The Community Disruption Case Study assesses the economic impacts of storm surge in the Oak Bay / Windsor
Park Focus Area (see Figures for Focus Area 15 in Appendix A Map Book). A storm surge event that inundates the Oak Bay Focus Area has the potential to disrupt the life of local residents. Inundation of the neighborhood may result in disruption of utility service, longer commute times due to flooded roads, higher costs to deliver emergency services, the closure of recreation areas, and in the long run, lower property values and tax receipts because of flood risks. For some SLR and storm surge scenarios the inundation could occur in a way that makes the south-eastern portion of this area into a temporary “island”. Without any management measures in place (e.g. to maintain a corridor of unflooded roads), this could prevent access to and from this part of the area. The following impacts were considered: Emergency Services costs, commute costs, residential utility disruption costs, fiscal risk. Three additional indicators (business disruption, recreation disruption, and transit disruption) are assessed in qualitative terms.
For the 24 Focus Areas used for this project the total valuation of land and improvements (as defined by BC Assessment) for the 2100 + 500-year storm surge scenario ranged from $333 million (for the Oak Bay Windsor Park SLR Focus Area) to $3.4 million (Albert Head SLR Focus Area). These are total asset values based on market valuation and do not infer expected losses that would occur from periodic inundation. Across the 24 SLR Focus Areas, BC Assessment data show that residential property has the highest total assessed value followed by commercial and then civic, institutional and recreational land uses.

## Slide 25: Case Study: Coastal Sea Level Rise Risk Assessment Capital Regional District (Victoria, BC)
Indicator | Metric | Data Inputs
Commute Costs | Daily cost of lost time per worker | Number of vehicle trips per day
 |  | Additional travel time required per trip from route impairment
 |  | Average dollar value per hour of a commuter’s time
Private Transit Costs | Daily cost of lost business revenue from service disruption | Average daily passengers
 |  | Average revenue per passenger
Tourism Costs | Daily cost of lost tourism spending | Average daily visitors (provincial and national parks)
 |  | Daily spending per visitor (provincial and national parks)
Emergency Services Costs | Daily cost of alternative emergency services | # of emergency response events per day
 |  | Additional cost of air versus road response per event
Fiscal Costs | Daily cost of lost sales tax revenue | Output from “Tourist Costs” metric
 |  | Provincial sales tax rate
Notes: Sea Level Rise Risk Assessment- Victoria, BC [cont.] [4/4]
This is a continuation of the Victoria, BC case study.
This table shows the indicator, metric and data inputs that were used for the Community Disruption Case Study

## Slide 26
Developing and Evaluating Adaptation Solutions

## Slide 27: California State Route 37 – North San Francisco Bay Sea Level Rise Vulnerability Study and Adaptation
Conceptual engineering design and costs for three structural alternatives to raise road
Conceptual renderings of alternatives
Notes: Sea Level Rise Adaptation Case Study – California [1/4]
Speaker Notes:
Highway 37, which runs along North SF Bay is vulnerable to the effects of SLR. This project conducted a sea level rise vulnerability and risk assessment for the 20-mile long highway. The project included SLR inundation mapping and a shoreline vulnerability assessment, which identified low-lying segments of levees that are responsible for protecting the highway from flooding. The project also developed conceptual level engineering design and cost estimates for alternatives to raise the highway, and 3-D renderings of proposed solutions.

## Slide 28: Existing Conditions
Notes: Sea Level Rise Adaptation Case Study – California cont. [2/4]
Speaker Notes:
This is a photo of the current road conditions at Highway 37. It is low-lying and prone to flooding. At this location the highway is surrounded by vegetated tidal saltmarsh.

## Slide 29: Alternative: Roadway on embankment
Notes: Sea Level Rise Adaptation Case Study – California cont. [3/4]
Speaker Notes:
One adaptation option for Highway 37 is that the road would be raised by fill, creating an embankment. The highway would run along the top of the embankment. This alternative is less expensive than the structural alternatives; however, it could be more difficult to permit due to wetland impacts and may experience problems with settlement due to consolidation of the underlying soils.

## Slide 30: Alternative: Roadway on causeway
Notes: Sea Level Rise Adaptation Case Study – California cont. [4/4]
Speaker Notes:
Another adaptation option for Highway 37 is that the road would built on piles, so that floodwaters would pass under the road. This alternative provides a unique opportunity to reconnect the hydrology of the wetlands surrounding the highway and may be advantageous from a restoration standpoint; however, elevating the highway on a structure is more expensive than the embankment alternative.
Source: http://hwy37.ucdavis.edu

## Slide 31: Climate Change and Extreme Weather Adaptation Options
Development of long list (125) adaptation strategies
Multi criteria analysis to select 5 strategies for concept design development
Examples of Final Strategies:
Living levee (coastal) and breakwater
Living levee (creek)
Scope of work for drainage study
Guidance on mainstreaming climate adaptation into agencies
Notes: Sea Level Rise Adaptation Case Study – Bay Area, California [1/4]
Speaker Notes:
The Climate Change and Extreme Weather Adaptation Options study was a climate change vulnerability assessment focusing on transportation infrastructure in the San Francisco Bay Area. The study developed a comprehensive list of 125 adaptation strategies that were evaluated using a multi-criteria analysis to select 4 focus strategies for concept design development. The focus strategies included a living levee/breakwater along the bay shoreline, a living levee along a tidal creek, a drainage study, and guidance on mainstreaming climate adaptation in agency processes. One of the focus areas selected was the San Francisco-Oakland Bay Bridge touchdown/toll plaza for development of a conceptual level engineering design and cost estimate of a living levee and breakwater (highlighted in subsequent slides).
________________________________________________________________________________________________________________
Name of Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area: Pilot Project
Author: San Francisco Bay Area Metropolitan Transportation Commission
Type of Resource: Pilot study report
Why read this document? For details on carrying out sea level rise assessments, use of shoreline overtopping analysis to identify areas for focused study; how to assess the sources, mechanisms, and timing of inland inundation and flooding; how to develop evaluation criteria to choose qualitatively between different adaptation strategies; details on living levees as an adaptation strategy; and how to mainstream climate change into an agency’s function
Topics covered: Sea level rise mapping, vulnerability assessment, evaluation criteria development, adaptation strategy development
Sector: Transportation
Stressors covered: Sea level rise and storm surge
Highlighted sections: The Executive Summary provides a good overview of the whole study. Chapters 5 and 6 outline design of living levees as adaptation strategies; Chapter 8 outlines how to mainstream climate adaptation into transportation agencies. Appendix B provides technical details on work carried out to identify the key areas of vulnerability that exist within three focus areas and assess the sources, mechanisms, and timing of inland inundation and flooding to inform the development of adaptation strategies.
Weblink: http://mtc.ca.gov/tools-and-resources/digital-library/climate-change-and-extreme-weather-adaptation-options
CAKE Link: http://www.cakex.org/directory/organizations/metropolitan-transportation-commission

## Slide 32: Living Levee Radio Beach
Living Levee
Notes: Sea Level Rise Adaptation Case Study – Bay Area, California cont. [2/4]
Speaker Notes:
This figure shows the placement of the living levee, which will be placed along the bridge touchdown and protect the westbound lanes of I-80, including the toll plaza, from 36 inches of SLR (2100 mid-range SLR projection). Other things to consider is that this levee would require that the dirt access road currently adjacent to I-80 be moved to the top of the levee.
The living levee design followed the guidelines and specifications in (USACE 1994) and (CDWR 2012).
However, it is noted that placement of the access road on top of the levee could inhibit access to the radio towers and other infrastructure in this vicinity. It is possible that a separate levee will be required to elevate and protect the north-south dirt road used to access the radio towers. This infrastructure is owned and operated by the Port of Oakland and access needs should be vetted with the city and other stakeholders before proceeding further in the conceptual design process.

## Slide 33: Living Levee Radio Beach
In this design, the existing access road is moved to the crest of the levee.
As the levee itself will not compensate for lost beach and marsh habitat due to SLR, it is recommended that sandy beach or marsh sediment be subsequently placed seaward of the levee.
Appropriate beach grass or marsh plants could be planted in this area
Living Levee
9.8
14.8
Notes: Sea Level Rise Adaptation Case Study – Bay Area, California cont. [3/4]
Speaker Notes:
In this cross section of the levee at Radio Beach, we can see that the access road is moved to the crest of the levee and the bayside bank of the levee is used as marsh and transitional habitat. However the levee will not compensate for lost beach and marsh habitat due to SLR, so it is recommended that sandy beach or marsh sediment be subsequently placed seaward of the levee.

## Slide 34: Living Levee Radio Beach – Cost Estimate
Breakwater
Protected Area
 | ITEM | UNITS | QUANTITY | UNIT PRICE | ITEM PRICE
1 | Project Mobilization/Demobilization (10% of base construction cost) | % | 10 |  | $266,250
2 | Clearing & Demolition/Disposal | LS | 1 | $170,000 | $170,000
3 | Signage and Traffic Control | LS | 1 | $15,000 | $15,000
4 | Survey | LS | 1 | $20,000 | $20,000
5 | Levee Construction | LF | 3,500 | $625 | $2,187,500
6 | Levee Road Construction | SY | 7,000 | $18 | $126,000
7 | Plantings (in Place) | SY | 16,000 | $9 | $144,000
 | Sub-Total 1: Estimated Base Construction Cost: |  |  |  | $2,928,750
 | Sales Tax @ 8.75% of Base Construction Cost |  |  |  | $256,266
 | Sub-Total 2: Estimated Base Bid: |  |  |  | $3,185,016
 | Permitting and Design (12% of base construction cost) | % | 10 |  | $351,450
 | Bidding/Contract Admin/Construction Oversight (10% of base construction cost) | % | 10 |  | $292,875
 | Concept Level Contingency (25% of Project Costs) | % | 20 |  | $732,188
 | Total Estimated Project Cost: |  |  |  | ~$4.6 Million*
Notes: Sea Level Rise Adaptation Case Study – Bay Area, California cont. [4/4]
Speaker Notes:
A rough cost estimate was conducted as part of the conceptual design for the living levee at Radio Beach. The development of conceptual level designs and cost estimates make the development of adaptation solutions more tangible for stakeholders. It is also important to have engineers evaluate the feasibility of different proposed solutions to provide more credibility to the study.

## Slide 35: Toronto: Ahead of the Storm: Preparing for Climate Change
Notes: Climate Change - Precipitation Storm Case Study – Toronto, Canada [1/2]
Speaker Notes:
In 2005, Toronto experienced a large storm which washed out a part of street and caused flash flooding to creeks, rivers and ravines, eroded streambanks and damaged trees and parks. More than 42,000 basements were flooded and the estimated damage to public and private property was $400-500 million – the most expensive storm in Toronto’s history. This was one of the eight extreme weather events in the past 20 years.
As a response to that storm, Toronto developed a climate change adaptation strategy report “2008 Ahead of the Storm: Development of a Climate Change Adaptation Strategy Report”.
The report outlines a 25-year plan designed to reduce flooding from intense rainfall, water quality degradation, and erosion impacts on streams and lake water. It uses information from the 2005 storm to guide the implementation of the plan.

## Slide 36: Toronto ‘Asking the Resiliency Question’
Source Control
Green Roof Incentive Program
Tree Planting
Mandatory Downspout Disconnection
Public Education
Rainwater Harvesting Demonstration Project
Establishing network of community and business partners
to work together to prevent stormwater pollution
Celebrating and rewarding partners who help
promote and contribute to solutions
‘End-of-pipe’ Treatment
Treatment ponds and wetlands
Stream and Aquatic Habitat Restoration
Notes: Climate Change - Precipitation Storm Case Study – Toronto, Canada cont. [2/2]
Speaker Notes:
Climate Adaptation Strategies for Toronto were divided into different elements:
- Source control strategies
- End of pipe treatments
- Public education
All of these strategies include the implementation of green infrastructure.
Benefits of GI are generally related to their ability to moderate the impacts of extreme precipitation or temperature and include
- Better management of stormwater runoff
- Lower incidents of combined storm and sewer overflows (CSOs)
- Water capture and conservation
- Flood prevention
- Storm-surge protection
- Defense against sea level rise
- Accommodation of natural hazards (e.g. relocating out of floodplains)
- Reduced ambient temperatures and urban heat island (UHI) effects.
Furthermore, most GI practices provide co-benefits to climate mitigation goals by helping to reduce GHG emissions.
The “2008 Ahead of the Storm: Development of a Climate Change Adaptation Strategy Report” recognized that GI technologies provide the most resilient solution to continually more unpredictable weather patterns (as opposed to concrete pipes and tanks sized to particular storms)
Although local governments and communities are using GI to achieve a variety of environmental and economic goals, including resilience to climate change, application of GI solutions are not yet widespread as adaptation best practices. Meanwhile, communities that have embraced GI may not have connected it with adapting to climate change, or, if they have, they may not possess the necessary capacity, know-how, or resources to plan and implement solutions.
“Asking the resilience question” means that local planning and building decisions need to incorporate how to prepare climate change impacts and weather extremes. When implementing GI solutions this means that local governments and property owners seek to understand the additional benefits these practices may have for adapting to climate change and for building resilient communities
Document: April 2008 - http://www.climateneeds.umd.edu/reports/Toronto%20City-Preparing%20Toronto%20for%20Climate%20Change.pdf
City of Toronto Wet Weather Flow Master Plan
(as mentioned in Ahead of the Storm, Preparing Toronto for Climate Change: Development of a Climate Change Adaptation Strategy 2008 document)
Stressors covered: Increasingly intense, unpredictable, storms
Project components: Green infrastructure to increase resiliency to more intense storms
Location: Toronto, Canada
Overview: The 25-year plan is designed to reduce flooding from intense rainfall, and water quality and erosion impacts on streams and lake water. Toronto Water is using information from the August 19, 2005 storm to guide its implementation of the plan. Source controls several GI measures including downspout disconnect, green roof incentive pilot program, rainwater harvesting demonstration project, tree planting and surface treatment ponds and wetlands.
Project Funding: City of Toronto
Weblinks:
http://www1.toronto.ca/wps/portal/contentonly?vgnextoid=d4e249983587f310VgnVCM10000071d60f89RCRD&vgnextchannel=972bab501d8ce310VgnVCM10000071d60f89RCRD#Beach
http://www.climateneeds.umd.edu/reports/Toronto%20City-Preparing%20Toronto%20for%20Climate%20Change.pdf
Other Case Studies:
Chicago, IL - Green Urban Design (GUD) Plan
Portland, OR – Investing $8M in GI to save $250M in hard infrastructure costs, with recognition that GI is flexible and scalable as climate conditions vary or change in the future
Fort Lauderdale – Introducing GI for Coastal Resilience
Micoud, Saint Lucia - http://www.stlucianewsonline.com/funding-approved-for-climate-change-adaptation-through-rainwater-harvesting-project/

## Slide 37: New York City Green Infrastructure Plan
“Multi-pronged sustainability effort that will reduce the urban heat island effect, enhance recreational opportunities, improve quality-of-life, restore ecosystems, improve air quality, save energy, and mitigate and adapt to climate change.”
GI is recognized as the most appropriate tool for supporting this effort, offering co-benefits above and beyond what traditional grey infrastructure can provide, often at a lower cost.
Notes: Green Infrastructure Case Study - New York [1/2]
Speaker Notes:
In September 2010, New York City released the NYC Green Infrastructure Plan, which presents an alternative approach to improving water quality that integrates “green infrastructure,” such as rain gardens and green roofs, with investments to optimize the existing system and to build targeted, cost-effective “grey” or traditional infrastructure.
The subtitle of the Green Infrastructure Plan is ‘A Sustainable Strategy for Clean Waterways,’ but beyond water quality, the Plan seeks to achieve multiple benefits including climate adaptation via a: “Multi-pronged sustainability effort that will reduce the urban heat island effect, enhance recreational opportunities, improve quality-of-life, restore ecosystems, improve air quality, save energy, and mitigate and adapt to climate change.’
The Plan recognizes GI as an effective response to a variety of environmental challenges that is cost-effective, sustainable and provides multiple desirable outcomes
The effort is led by Mayor’s office and Dept. of Environmental Protection in collaboration with many City agencies including:
  Dept. of Transportation (DOT)
  Dept. of Parks and Recreation (DPR)
  Dept. of Design and Construction (DDC)
  Dept. of City Planning (DCP)
  Dept. of Education (DOE)
  Dept. of Sanitation (DSNY) Dept. of Citywide Administrative Services (DCAS)
  Dept. of Housing and Preservation and Development (HPD)
  New York City Economic Development Corporation (EDC)
  New York City Housing Authority (NYCHA)

## Slide 38: New York City: Green Infrastructure Plan GI as a base for mitigation to and adaptation to Climate Change
Reduce Urban Heat Island (UHI) Effect
Improve Quality of Life
Enhance Recreational Opportunities
Restore Ecosystems
Improve air quality
Save energy
Improve Water Quality
Manage Flooding
Increase Property Values
Reduce and Reuse Water
Notes: Green Infrastructure Case Study - New York cont. [2/2]
Speaker Notes:
Green Infrastructure (GI) will improve performance (e.g. est. 2 billion gallons less CSO volumes) while reducing the City’s sewer management costs by $2.4 Billion over 20 years
Philadelphia, like NYC, has also determined GI is more cost effective than continued investment in grey infrastructure in the long-term AND provides all the above mentioned co-benefits which both mitigate climate change (e.g. reduce GHG emissions, reduce energy use, reduce water use) and increase overall resiliency.
It is estimated that every fully vegetated acre of GI will provide:
  total annual benefits of $8,522 in reduced energy demand
  $166 in reduced CO2 emissions
  $1,044 in improve air quality
  $4,725 in increased property value

## Slide 39: Chicago - Existing Green Infrastructure
Policies
Chicago Stormwater Ordinance (2008)
Sustainable Development Policy (2004, 2008)
Adding Green to Urban Design (2008)
Sustainable Urban Infrastructure Guidelines (2013)
Programs
Green Roofs Initiative
Green Alleys
Green Streets
Downspout Disconnections
Sustainable Backyard Program
Notes: Green Infrastructure Case Study – Chicago [1/2]
Speaker Notes:
Chicago has experience 4 10-yr storm events in the last 6 years, as defined by the Illinois state climatologist. This implies that a new normal/benchmark is needed to define storm frequencies.
A 2008 study found that Chicago would be impacted by higher temperatures, more precipitation and more frequent and intense storms with most of the increased precipitation anticipated for the winter and spring.
Green infrastructure is a key tool in the stormwater management plan. Existing policies and programs are:
- Chicago stormwater ordinance (2008)
- Sustainable development policy (2004,2008)
- Adding green to urban design (2008)
- Sustainable urban infrastructure guidelines (2013)
- Green Roofs Initiative
- Green Alleys
- Green Streets
- Downspout Disconnections
- Sustainable Backyard Program
For more information: http://www.cityofchicago.org/content/dam/city/progs/env/ChicagoGreenStormwaterInfrastructureStrategy.pdf

## Slide 40: Chicago - Green Stormwater Infrastructure Strategy
Minimize basement flooding in Chicago’s most impacted neighborhoods
Reduce pollution to Chicago’s rivers and Lake Michigan
Enhance environmental quality through water infrastructure investments
Increase the city’s resilience to extreme rain events and climate change
FOUR Long-term Goals
Capital Projects
Permeable Streets
Bioswales
Green Stormwater Infrastructure Study
Rainfall Frequency Analysis
Citywide Stormwater Management Plan
FIVE Principal Initiatives
Notes: Green Infrastructure Case Study – Chicago cont. [2/2]
Speaker Notes:
The 2014 Green Stormwater Infrastructure Strategy builds on these prior programs and policies by pursuing two main objectives:
- committing additional public funding to build GI infrastructure
- launching studies to determine long-term role that GI can play alongside grey infrastructure to address city’s rainfall runoff challenges
Principal initiative are:
Capital Projects – will allocate $50M over next five years to build more GI, especially into existing and future public capital projects including: upgrading water pipes, repairing roads, building parks, constructing public facilities and renovating schools
Permeable Streets - over next decade will be replacing 880 miles of water mains and 250 miles of sewer mains. rather than replace with standard asphalt, will incorporate permeable pavement for main travel, bike and/or parking lanes
Bioswale – continue to invest in street trees and green streets: primary benefits being cleaning air, reducing energy use, minimizing UHI and enhancing property value; The Depts. of Water Management, Transportation and Street and Sanitation will work together to develop standard specs and guidelines to ensure successful implementation and maintenance
GI Study – have learned a lot in last ten years but need additional data and analysis to determine the appropriate type, amount and location of GI stormwater infrastructure to address our challenges in the future; additional work is needed to determine best balance between green and grey in the long-term; will evaluate full costs and benefits specific to Chicago and then evaluate various scenarios for a large-scale implementation of GI citywide and by neighborhood, specifically in achieving goals such as reducing basement flooding risk and improving water quality
Rainfall Frequency Analysis - incorporate advanced modeling and best science available to consider future climate conditions, not just historical rainfall patterns: if build infrastructure (water and sewer mains) to last 100 years, “we should also consider what climate may exist at the end of the century and develop a stormwater management strategy that confronts this challenge”
2015 Citywide plan should be informed by the aforementioned Cost-Benefit analysis of GI and Climate Change studies
For more information- http://www.cityofchicago.org/content/dam/city/progs/env/ChicagoGreenStormwaterInfrastructureStrategy.pdf

## Slide 41: Case Study: Coastal Adaptation Louisiana Coastal Master Plan
1880 square miles of land loss since 1930s and a potential loss of 1750 square miles if no action taken
In response to Katrina, legislature created the Coastal Protection and Restoration Authority of Louisiana, and required it to developed a master plan for a safe and sustainable coast.
Image shows flooding depths for a 100 year flood 50 years from now
Image Source: Louisiana’s Comprehensive Master Plan for a Sustainable Coast (2012)
Notes: Coastal Adaptation Case Study – Louisiana [1/2]
Speaker Notes:
In response to Katrina, state legislature created the Coastal Protection and Restoration Authority of Louisiana, and required it to develop a master plan for a safe and sustainable coast.
There has been 1880 square miles of coastal land loss since the 1930s, and a future potential loss of 1850 square miles if no action is taken. Also, if no action is taken now, expected annual damages from coastal flooding will be $23.4 billion, which is ten times greater than todays figure.
Image from pdf of masterplan: https://www.doi.gov/sites/doi.gov/files/migrated/deepwaterhorizon/adminrecord/upload/CPRA-Louisiana-s-Comprehensive-Master-Plan-for-a-Sustainable-Coast-2012.pdf

## Slide 42: Strategies recommended in Master Plan
Living Levee
2012 Masterplan identifies $50 billion worth of projects aimed at protecting and restoring the coastline
Required levees and large diversions, but also included restoration of natural features such as marshes, oyster barrier reefs and ridge restoration
Plan included non-structural elements such as land use planning; also raising residential structures and flood-proofing for small amounts of flooding
Notes: Coastal Adaptation Case Study – Louisiana cont. [2/2]
Speaker Notes:
The 2012 Masterplan identifies $50 billion worth of projects aimed at protecting and restoring the coastline. It included major upgrades to current levee systems (most of which have already been constructed) and also includes restoration of natural features such as marshes, oyster barrier reefs and ridge restoration
It is a multi-pronged approach of protection, restoration and adaptation:
Protect critical elements with structural measures (levees)
Restore natural elements that help with flood protection (marshes, barrier reefs)
Adapt to rising waters and occasional flooding (elevating houses, land-use planning)
The images shows already completed and future proposed projects for the LO coastline. Projects are characterized by their type:
Structural protection
Bank stabilization
Oyster barrier reef
Ridge restoration
Shoreline protection
Infrastructure
Terraces
Barrier island restoration
Marsh creation
Sediment diversion
Hydrologic restoration
Data from LO 2012 Masterplan
http://coastal.la.gov/a-common-vision/2012-coastal-master-plan/
https://issuu.com/coastalmasterplan/docs/coastal_master_plan-v2?layout=http://coastalmasterplan.la.gov/issuu/mpmar2012/layout.xml&e=3722998/2447530
Image from pdf of masterplan: https://www.doi.gov/sites/doi.gov/files/migrated/deepwaterhorizon/adminrecord/upload/CPRA-Louisiana-s-Comprehensive-Master-Plan-for-a-Sustainable-Coast-2012.pdf

## Slide 43
Integrating Climate Change into Planning and Operations

## Slide 44: Vancouver, British Colombia
Meeting Flood Construction Levels (FCL) through the placement of fill and/or structural means
Restricting development near the water and requiring buildings to be setback
Providing adequate drainage systems
Implementing flood resilient construction measures to reduce the damage caused from flooding and reduce the recovery time from flood events
Resilience against future flooding
Notes: Climate Change Planning Case Study – Vancouver, BC, Canada [1/3]
Speaker Notes:
The current and anticipated impacts of climate change will affect the city in many ways. SLR will continue to increase flood risk along the City coastline, including the North Arm of the Fraser River.
The City of Vancouver has several ways to achieve flood resilience:
With respect to meeting Flood Construction Levels (FCL), to address increased flood risk, buildings built today should be designed for flood resilience throughout their lifespan. City flood-proofing standards required revision to incorporate anticipated sea level rise in line with the new Provincial guidelines and current scientific consensus.
Flood Construction Levels intended to:
reduce or prevent injury, human trauma, and loss of life in the case of flood
to minimize property damage during flooding events, and
to reduce the amount of time it takes to return to operational functionality when flood waters recede

## Slide 45: Vancouver, British Colombia
Section 306(cc) of Charter allows Council to make bylaws
Building code bylaw allows Council to:
  Withhold building permits for parcels in designated floodplains until satisfactory design is achieved
  Requires a covenant registered against the land acknowledging the risk of flood damage
Adaptable policy
Notes: Climate Change Planning Case Study – Vancouver, BC, Canada cont. [2/3]
The City developed their own building code bylaw, that allows the City to withhold building permits for parcels in designated floodplains until satisfactory design is achieved and risk is acknowledged.
Vancouver is the only municipality in British Columbia that can do this; other municipalities must use the Provincial building code

## Slide 46: Vancouver, British Colombia
Sept. 2014 raised flood construction levels (FCL) requirements to 4.5m, 1m over previous level, due to projected SLR
Based on 2011 Provincial Guidelines; to protect people from flood risk to the year 2100 during storm events at high tide with a likelihood of recurrence of once every 500 years
Proactively reducing future flood damage and minimizing estimated $9.5 Billion required to adapt city to projected 2100 water levels
Updating Policy to account for future SLR
Notes: Climate Change Planning Case Study – Vancouver, BC, Canada cont. [3/3]
Timeline for new Flood Construction Levels (FCL).
In January 2012, staff began encouraging interim FCLs 1m above existing levels (new level: ~4.5m) in response to the Provincial Guideline issued by the Ministry of Environment based on updated global and local climate impact models. The interim levels provided an opportunity to signal the coming change and work proactively with the development and building community to understand impacts and prepare for change.
On July 25, 2012, City Council approved the Climate Change Adaptation Strategy recommending that staff undertake priority actions including an amendment to the Flood-Proofing Policies & FCL.
May 2014 Council Report making the case for the change: http://council.vancouver.ca/20140709/documents/cfsc2.pdf
Sept 2014 – new FCL Approved - Current requirements: http://former.vancouver.ca/commsvcs/guidelines/F014.pdf
  The flood plain standards apply to all lands designated as flood plains and subject to flood construction level (FCL) requirements. Further review and revision of the designated flood plain areas and associated regulations is anticipated as global sea level rise and storm surge projections are refined over time and local impacts are better understood.
  The underside of a floor system (wood or steel) or the top of a concrete slab of any building used for habitation, business or storage of goods shall not be lower than 4.6m from GVRD datum in designated flood plains as outlined on Diagrams A1and B, in Appendix B of this document.
  The FCL was calculated following the methodology introduced in the Provincial Guidelines (2011). It is designed to protect people and property from anticipated flood risk to the year 2100 during storm events at high tide with a likelihood of recurrence of once every 500 years (1:500 year return period).This translates to a 0.2% chance of occurring in any given year and is a design standard for dense urban areas.
  City staff consulted with the Urban Development Institute, the Association of Professional Engineers and Geoscientists of B.C. the Architectural Institute of B.C., engineering and surveying professionals, the Real Estate Foundation, Port Metro Vancouver, BC Ministry of Lands and Natural Resources Operations, Metro Vancouver, Canada Mortgage And Housing Corporation (CMHC), NRCan, CP Rail, CN Rail, insurance companies, other planning and design community professionals, and multiple neighbouring municipalities, among other organizations on the approach outlined in this report.
Provincial study estimated the cost to build flood protection infrastructure in Metro Vancouver (from coastal shoreline and the Fraser river shoreline as far east as the Port Mann Bridge), to meet the projected water level in the year 2100, at $9.5 billion. Vancouver’s proactive approach to instituting appropriate FCLs now will reduce future flood damage and may avoid some of these projected infrastructure costs.

## Slide 47: Fort Lauderdale, Florida
Flexibility and Resilience are foundational cornerstones of the City’s 2035 Vision and Strategic Plan
Organized the Plan within Cylinders of Excellence and Internal Support Platform, i.e. strategic area teams
Interdepartmental teams work together to achieve the 12 goals and 38 objectives identified in the Plan
City maintains a flexible decision making model in order to respond to new data
Regularly reach out to community to understand needs
Mainstreaming Resiliency
Notes: Climate Change Planning Case Study – Ft. Lauderdale, Florida
Speaker Notes:
In 2012 Fort Lauderdale suffered extensive damage when seasonally high tides coincided with the effects of Sandy. Following these events the City implemented adaptive measures to ensure the sustainability of the City’s infrastructure, from utility distribution systems to bridges and roadways.
The City responded by joining forces with Broward County and numerous regional parties to take a comprehensive look at climate change. They concluded, without reservation, that it was now necessary to factor the projected climate change impacts into all of the City’s functions, and, most importantly, to implement programs and projects to response to those anticipated impacts.
  The city developed the 2035 ‘Fast Forward Fort Lauderdale’ Strategic Plan that guides all City activities.
  The Plan is the community's long-term aspiration for the future of Fort Lauderdale; Press Play Fort Lauderdale 2018 is the first five year journey to that Vision.
  Press Play Fort Lauderdale 2018 is organized within the Cylinders of Excellence and Internal Support Platform, a set of strategic area teams, all of which bring focus and coordination to what they do every day: build community.
  As interdepartmental teams, the Cylinders and Platform work together to achieve a set of 12 aspirational goals and 38 objectives identified in the plan.
  Examples of resiliency objectives:
  reduce flooding and adapt to sea level rise
  improve climate change resiliency by incorporating local, regional and mega-regional plans
  secure our community’s water supply
  Examples of resiliency measures achieved:
  Developed a comprehensive and advanced water sustainability program, including extensive recycled water network and rainwater harvesting, so that long-term water supply is no longer an area of concern
  Established a beach nourishment and seeding program that is a true recycling system, through which no new sand is ever required, that preserves the City’s near-shore ecological system.
  The program is now used by cities throughout the globe
  Replaced fatigued infrastructure with more resilient and permeable system that was engineered to withstand the effects of climate change

## Slide 48: Baltimore Floodplain Management
3 of top 10 recorded storms (since 1912) occurred in past five years
Floodplain code amended in 2015 (Article 7, Natural Resources)
Floodplain regulations in Baltimore now exceed State and Federal floodplain regulations
Established Baltimore City Floodplain Management Office
Amended Floodplain Code
Notes: Climate Change Planning Case Study – Baltimore, Maryland [1/2]
Speaker Notes:
Baltimore City is built at the mouth of the Patapsco River, which empties directly into the Chesapeake Bay. Presently, the City’s regulated floodplain is 5,136 acres and contains over 2,800 buildings.
Floodplain regulations in Baltimore were created to protect life, health, and property while minimizing need for rescue and relief, economic interruption, and damage to infrastructure. These regulations supersede both State and Federal floodplain regulations
The Federal Emergency Management Agency (FEMA) produces Flood Insurance Rate Maps (FIRM) which identify areas that are at risk of flooding. FIRMs include statistical information such as data for river flow, storm tides, hydrologic/hydraulic analyses, and rainfall and topographic surveys. Flood hazard areas identified on the Flood Insurance Rate Map are identified as a Special Flood Hazard Area (SFHA). In Baltimore City, the regulated floodplain includes the 1% and 0.2% annual-chance flood areas, also known as the 100-year and 500-year floodplain.
The City of Baltimore changed the floodplain code:
  We regulate to the 500-year extent citywide and to whichever is higher between the 100-year Stillwater elevation or the 500-year elevation in the coastal floodplain (called our flood resilience area). We also adopted ASCE-24 into our code and do not exempt historic structures. We do work on recommending floodgates, flood-proofing materials and special considerations for historic property flood-proofing, but on a case by case basis.

## Slide 49: Baltimore Floodplain Management
Notes: Climate Change Planning Case Study – Baltimore, Maryland [2/2]
Speaker Notes:
Baltimore has its own Floodplain Management Program.
The BaltimoreSustainability.org website empowers citizens to be proactive and has a lot of useful information on the floodplain management program
CityView is the City of Baltimore’s mapping portal that provides information on a series of topics of interest for its citizens, visitors, researchers, and business community. This site will be updated with refreshed data and new layers on a frequent basis and feedback from its users will be an important source for making the application more useful to all.
Featured topics include:
trash and recycling pick up
alley sweeping
flood plains and contours
weather

## Slide 50: Boston, Massachusetts Climate Preparedness Checklist
Projects subject to Zoning Code have to:
  complete a Climate Change Preparedness and Resiliency Checklist
  provide any necessary responses regarding project resiliency, preparedness, and to mitigate any identified adverse impacts that might arise under future climate conditions
The checklist:
  provides a framework for considering present and future climate conditions in assessing projects’ environmental impacts
  is updated to reflect the most current climate change information, research and practices
  covers extreme weather (heat, wind, rain..), and sea level rise / coastal flooding
Notes: Climate Change Planning Case Study – Boston, Massachusetts
Speaker Notes:
In Nov. 2013, in conformance with the Mayor’s 2011 Climate Action Leadership Committee’s recommendations, the Boston Redevelopment Authority (BRA) adopted policy for all development projects subject to Boston Zoning Article 80, including all Institutional Master Plan modifications and updates, to complete a climate preparedness checklist.
Checklists are due at the time of initial project filing or Notice of Project Change and final filing just prior to seek Final BRA Approval.
Checklist considers:
  Extreme weather: e.g. days over 90 degrees likely to increase from 10 to 64 by end of century, increase in storm volumes and intensities, per Boston Water and Sewer Commission (BWSC) projections
  Sea Level Rise: currently refers to 2013 report of the Massachusetts Office of Coastal Zone Management (CZM) Sea Level Rise: Understanding and Applying Trends and Future Scenarios for Analysis and Planning; IGBC recommends developers to plan for intermediate high scenario and the highest scenarios for critical facilities and infrastructure (4.2 to 6.8 ft by 2100)
Article 37 establishes the Interagency Green Building Committee (IGBC) to advise the Boston Redevelopment Authority (BRA) and the Inspectional Services Department (ISD) on project compliance with the City's green building and climate-change policies and requirements. Reviews for compliance occur at three phases: Initial Filing, Design/Building Permit Filing, and Construction/Certificate of Occupancy Filing (see Boston Green Building & Boston Climate Preparedness and Resiliency Review Procedures and Submittal Requirements). The BRA and ISD rely on the IGBC’s advice for the approval of projects and the issuance of Building Permits and Certificates of Occupancy.
Name of Resource: Climate Change Preparedness and Resiliency Checklist
Author: City of Boston
Type of Resource: Checklist
Why read this document?
In Nov. 2013, in conformance with the Mayor’s 2011 Climate Action Leadership Committee’s recommendations, the Boston Redevelopment Authority (BRA) adopted policy for all development projects subject to Boston Zoning Article 80, including all Institutional Master Plan modifications and updates, to complete a climate preparedness checklist. The six-page checklist is not specific to Boston and can be adapted as a tool for any developer to use, or City to encourage/require.
Topics covered: Building resilience measures
Sector: Private-sector large buildings
Stressors covered: Extreme weather, sea level rise and coastal flooding
Highlighted sections: The checklist is only six page and is worth reading through in its entirety.
Weblink: http://www.bostonredevelopmentauthority.org/getattachment/0518c9ed-8768-4481-883e-3d27ce5b56dd

## Slide 51: San Francisco SLR Capital Planning Guidance
2014: Capital Planning Guidance requires vulnerability assessment for projects in relation to vulnerability zone of 108” SLR (high end prediction +100 year storm event for 2100)
Required for projects over $5M in size
Detailed checklist provided to walk staff through assessment
Mitigation strategies required for projects of certain age, dollar value, vulnerability
Notes: Sea Level Rise Planning Case Study – San Francisco, California
Speaker Notes:
The City of San Francisco recently adopted sea level rise capital planning guidance to promote consistent consideration of the impacts of sea level rise on capital projects within the city. The guidance also includes a checklist for project managers to help them step through the process of incorporating consideration of sea level rise into their project planning and design.
See here for more information
http://onesanfrancisco.org/staff-resources/sea-level-rise-guidance/

## Slide 52: Miami Beach, Florida Code Modifications
Miami Beach is in the process of multi code changes in relation to:
Base Flood Elevation
Freeboard
Seawall Elevations
Yards
Staff are discussing changes to
City Design Storm
Stormwater Management: Quantity
Stormwater Management: Quality
Stormwater infiltration
Level of Service
Notes: Sea Level Rise Planning Case Study – Miami Beach, Florida [1/2]
Speaker Notes:
Miami Beach convened a Blue Ribbon Sea level Rise Panel in January 2014. The Panel oversees the City’s response to flooding (stormwater and sea level rise) and assisting with the implementation of a comprehensive flood management plan. The City of Miami Beach is pursuing a building code update to specify new building standards with respect to the FEMA Base Flood Elevation and seawall crest design elevations in addition to other updates.
More information here: http://www.miamibeachfl.gov/cityclerk/default.aspx?id=78270

## Slide 53: Miami Beach, Florida Code Modifications
Passed Ordinances |  |  | 
 |  | Existing Requirements | Proposed Requirements
1. | Base Flood Elevation (BFE) | 5.44 Feet NAVD (7 Feet NGVD) | 6.44 Feet NAVD (8 Feet NGVD)
2. | Freeboard | 0 feet above BFE | +1 to +5 feet above BFE
3. | Seawall Elevation (Private) | 3.2 FT NAVD 4.76 FT NGVD | 4 to 5.7 FT NAVD 5.56 to 7.26 FT NGVD
4. | Seawall Elevation (Public) | 3.2 FT NAVD 4.76 FT NGVD | 5.7 FT NAVD 7.26 FT NGVD
5. | Minimum required yard elevation | No minimum required | 5.0 Feet NAVD (6.56 Feet NGVD)
Notes: Sea Level Rise Planning Case Study – Miami Beach, Florida [2/2]
Speaker Notes:
The city of Miami Beach has been upgrading building codes that require new construction to raise the minimum height of city infrastructure, including raising roads. The City Council has approved increases to its base flood elevation requirements, increases in its sea wall elevation, and a minimum yard elevation. They apply only to new construction or renovations that change more than 50 percent of a building, and the new rules don’t yet apply to its two historic districts.

## Slide 54: MTC Report Chapter on Mainstreaming Climate Change Risk into Transportation Agencies
A formal policy statement on climate change adaptation should be initiated by top management.
Policy should lay the foundation for a comprehensive mainstreaming program
Policy makes a statement to State and federal policy makers and funders.
Policy establishes climate change as a critical challenge requiring coordinated agency-wide response
Guidance on Creating Overarching Climate Change Policy
Notes: Climate Change Planning Case Study – San Francisco Bay Area, California [1/4]
Speaker Notes:
In this project, one of the 5 adaptation strategies developed focused on providing process guidance on how transportation agencies can mainstream adaptation planning into their planning and operations. This chapter emphasizes the importance of an overarching climate policy which in turn drives various departments to better prepare for climate change.
Name of Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area: Pilot Project
Author: San Francisco Bay Area Metropolitan Transportation Commission
Type of Resource: Pilot study report
Why read this document? For details on carrying out sea level rise assessments, use of shoreline overtopping analysis to identify areas for focused study; how to assess the sources, mechanisms, and timing of inland inundation and flooding; how to develop evaluation criteria to choose qualitatively between different adaptation strategies; details on living levees as an adaptation strategy; and how to mainstream climate change into an agency’s function
Topics covered: Sea level rise mapping, vulnerability assessment, evaluation criteria development, adaptation strategy development
Sector: Transportation
Stressors covered: Sea level rise and storm surge
Highlighted sections: The Executive Summary provides a good overview of the whole study. Chapters 5 and 6 outline design of living levees as adaptation strategies; Chapter 8 outlines how to mainstream climate adaptation into transportation agencies. Appendix B provides technical details on work carried out to identify the key areas of vulnerability that exist within three focus areas and assess the sources, mechanisms, and timing of inland inundation and flooding to inform the development of adaptation strategies.
Weblink: http://mtc.ca.gov/tools-and-resources/digital-library/climate-change-and-extreme-weather-adaptation-options
CAKE Link: http://www.cakex.org/directory/organizations/metropolitan-transportation-commission

## Slide 55: MTC Report Chapter on Mainstreaming Climate Change Risk into Transportation Agencies
Integrate climate resilience into a variety of other policies, such as risk management, asset management, or sustainability, or
Develop a dedicated, standalone adaptation policy which will then influence all other policies.
Preferably, these approaches would be pursued concurrently, as complementary strategies
Pathways to Establishing Policy Framework
Notes: Climate Change Planning Case Study – San Francisco Bay Area, California cont. [2/4]
Following up on the previous slide, this slide provides specific pathways to establishing an overarching climate policy, either via the development of a stand-alone policy or via integration into existing overarching policies.
Name of Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area: Pilot Project
Author: San Francisco Bay Area Metropolitan Transportation Commission
Type of Resource: Pilot study report
Why read this document? For details on carrying out sea level rise assessments, use of shoreline overtopping analysis to identify areas for focused study; how to assess the sources, mechanisms, and timing of inland inundation and flooding; how to develop evaluation criteria to choose qualitatively between different adaptation strategies; details on living levees as an adaptation strategy; and how to mainstream climate change into an agency’s function
Topics covered: Sea level rise mapping, vulnerability assessment, evaluation criteria development, adaptation strategy development
Sector: Transportation
Stressors covered: Sea level rise and storm surge
Highlighted sections: The Executive Summary provides a good overview of the whole study. Chapters 5 and 6 outline design of living levees as adaptation strategies; Chapter 8 outlines how to mainstream climate adaptation into transportation agencies. Appendix B provides technical details on work carried out to identify the key areas of vulnerability that exist within three focus areas and assess the sources, mechanisms, and timing of inland inundation and flooding to inform the development of adaptation strategies.
Weblink: http://mtc.ca.gov/tools-and-resources/digital-library/climate-change-and-extreme-weather-adaptation-options
CAKE Link: http://www.cakex.org/directory/organizations/metropolitan-transportation-commission

## Slide 56: MTC Report Chapter on Mainstreaming Climate Change Risk into Transportation Agencies
Guidance on leveraging and adjusting existing systems and procedures in functional areas
Examples of functional areas
  Planning
  Capital Development
  Operations
  Administration
In each functional area, responsibilities and duties area paired with mainstreaming actions.
Integrating Climate Change into Agency Programs or Functional Areas
Notes: Climate Change Planning Case Study – San Francisco Bay Area, California cont. [3/4]
In this project, one of the 5 adaptation strategies developed focused on providing process guidance on how transportation agencies can mainstream adaptation planning into their planning and operations. This chapter provides specific examples of how the planning, capital development, operations, and administration departments can incorporate climate considerations in performing their responsibilities.
Name of Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area: Pilot Project
Author: San Francisco Bay Area Metropolitan Transportation Commission
Type of Resource: Pilot study report
Why read this document? For details on carrying out sea level rise assessments, use of shoreline overtopping analysis to identify areas for focused study; how to assess the sources, mechanisms, and timing of inland inundation and flooding; how to develop evaluation criteria to choose qualitatively between different adaptation strategies; details on living levees as an adaptation strategy; and how to mainstream climate change into an agency’s function
Topics covered: Sea level rise mapping, vulnerability assessment, evaluation criteria development, adaptation strategy development
Sector: Transportation
Stressors covered: Sea level rise and storm surge
Highlighted sections: The Executive Summary provides a good overview of the whole study. Chapters 5 and 6 outline design of living levees as adaptation strategies; Chapter 8 outlines how to mainstream climate adaptation into transportation agencies. Appendix B provides technical details on work carried out to identify the key areas of vulnerability that exist within three focus areas and assess the sources, mechanisms, and timing of inland inundation and flooding to inform the development of adaptation strategies.
Weblink: http://mtc.ca.gov/tools-and-resources/digital-library/climate-change-and-extreme-weather-adaptation-options
CAKE Link: http://www.cakex.org/directory/organizations/metropolitan-transportation-commission

## Slide 57: MTC Report Chapter on Mainstreaming Climate Change Risk into Transportation Agencies
Project Prioritization for Capital Improvements
Project Development/Scoping
Design Guidelines, Standards, and Specifications
Project Engineering
Permitting
Routine Asset Management
Capital Planning Components that should consider Mainstreaming
Notes: Climate Change Planning Case Study – San Francisco Bay Area, California cont. [4/4]
Following up on the previous slide, this slide offers examples of the responsibilities held by a specific department in transportation agencies (the capital planning department), that would be affected by climate change considerations.

## Slide 58: Port of Long Beach: Addressing climate change through policies & plans
Climate change language has been recommended for inclusion into the following Port documents:
Strategic Plan
Risk Assessment Manual
Guidelines for Professional Consulting Services
Project Delivery Manual
Quality Management System
  Stormwater Infrastructure Master Plan
  Design Criteria Manual
  Electrical Design Criteria and Standard Plans
The Port is also considering developing a Port climate change policy.
Notes: Climate Change Planning Case Study – Long Beach, California [1/2]
Speaker Notes:
In this project, one of the five adaptation strategies focused on incorporating recommended climate change language into Port policies, plans, and guidelines. The integration of climate change language into these key planning and design documents will ensure that future investments by the Port are safeguarded through consideration of climate impacts and incorporation of adaptation strategies to cope with changing environmental conditions.

## Slide 59: Port of Long Beach: Addressing climate change through guidelines
  Recommendations were made for the Port’s Harbor Development Permit (HDP) to consider climate change:
  New climate change checklist in the short and long HDP forms
  Port Coastal Vulnerability Zone map (36’’ SLR and 36’’ SLR + storm surge) added
  Staff guidance manual to support effective checklist review process
Notes: Climate Change Planning Case Study – Long Beach, California cont. [2/2]
Speaker Notes:
Another of the five adaptation strategies focused on updating the Port’s Harbor Development Permit (HDP) process to include climate change considerations. A new section in the HDP short and long forms is designed to heighten awareness and consideration of SLR impacts on any proposed development sites. A Port Coastal Vulnerability Zone map was created to clarify whether an applicant’s project is located in an area vulnerable to temporary or permanent inundation (36’’ SLR and 36’’ SLR + 100-year storm surge). A guidance manual was developed for Port staff to provide additional support to ensure that the HDP checklist is properly completed and reviewed.

## Slide 60: Baltimore Preparedness & Resiliency: CIP requirements
The strategies and actions of the Disaster Preparedness Project and Plan (DP3) must be considered and integrated into the Capital Improvement Program (CIP)
Notes: Climate Change Planning Case Study – Baltimore, Maryland [1/3]
Strategies and actions of the Disaster Preparedness Project and Plan must be considered in development of capital improvement projects.
Each department has a responsibility to consider how their projects will address future climate impacts, reduce risk, and make Baltimore more resilient.
Projects must integrate consideration for increased precipitation events, including heavier precipitation in shorter durations of time; higher heat including weeks of 90+ degree temperatures; stronger storms including hurricanes and strong winds; and rising sea levels which will lead to increased tidal flooding and storm surge.

## Slide 61: Baltimore Preparedness & Resiliency CIP requirements
Design bridge expansion joints for longer periods of high heat and heavy precipitation events, and develop a more robust inspection and maintenance process
Prioritize infrastructure upgrades for roads identified at risk of flooding through the use of elevation data and Sea, Lake and Overland Surges from Hurricanes (SLOSH) model results
Install external generator hookups for critical facilities that depend on mobile generators for backup power
Sample recommendations from Plan that impact capital projects
Notes: Climate Change Planning Case Study – Baltimore, Maryland cont. [2/3]
See slide for notes.

## Slide 62: Baltimore Preparedness & Resiliency CIP requirements
Install energy-efficient and low-water-use equipment during renovations in all City-owned buildings
Replace old and malfunctioning pipes with new pipes or retrofit existing pipes with new lining prioritizing areas with reoccurring flooding
Install backflow-prevention devices or other appropriate technology along waterfront to reduce flood risk
Sample recommendations from Plan that impact capital projects
Notes: Climate Change Planning Case Study – Baltimore, Maryland cont. [3/3]
See slide for notes.