## Slide 1: Climate Preparedness Training Toolkit Template
City of ____________

## Slide 2: Acknowledgements
Training was developed through a generous grant from the USDN Innovation Fund. The project was conceived and managed by Kristin Baja, City of Baltimore, and Tracy Morgenstern, City of Seattle, and developed and produced by AECOM.
Thanks to staff from the cities of Baltimore, Fort Lauderdale, Providence, Seattle, Toronto, and Vancouver for helping to develop and pilot the training.

## Slide 3: Agenda
4. Climate Change Adaptation Process
3. Climate Hazards and Impacts
5. Review Climate Science
6. Climate Change Projections
7. Asset and Operations Inventory
8. Assess Vulnerability
9. Assess Exposure
1. Intro to Climate Change
2. Flooding Processes
10. Assess Risk
11. Developing and Evaluating Adaptation Solutions
12. Integrating Climate Change into Planning and Operations
Notes: Speaker Instructions:
Agenda can be revised depending on which modules the trainer retains in toolkit.

## Slide 4: Purpose and Goals of Training
Why are we here today?
Mainstreaming (or operationalizing) climate change preparedness and resilience into planning and engineering activities
Develop better understanding of climate change vulnerability and risk assessments so that city staff can conduct or assist in completion of these assessments
Notes: Speaker Notes:
The purpose of this training is to educate city staff about climate change and its impacts to city assets and operations. Climate change will affect many of the environmental hazards that our city currently considers during planning, design, construction, and maintenance of city assets and staff need to proactively address these challenges to maintain core city services and functions in a changing climate.
This training focuses on changes to riverine, urban, and coastal flooding as a result of climate change and provides tools, exercises, and case studies to educate staff, encourage cross-department collaboration, and promote incorporation of climate change and resilience considerations into day to day activities. Many of the topics covered in this training are focused on flooding hazards; however, the concepts can be applied to other climate change hazards as well. The goal of the training is to equip city staff with the knowledge and resources to “mainstream” or “operationalize” climate change preparedness and resilience into planning, engineering, operations, and maintenance activities.
Many cities are completing climate change vulnerability and risk assessments to better understand how climate change will impact their assets and operations. City staff are increasingly being asked to lead, manage, or participate in these assessments. This training also provides an overview of the climate change vulnerability and risk assessment process to build capacity for city staff to support these ongoing efforts and understand what type of data and other information may be requested of them as part of these assessments and why their participation is critical.

## Slide 5: Outline of Training
Training developed by the Urban Sustainability Directors Network (USDN) for use by member cities
Training offers two options:
      Game-based track
      Exercise-based track
  Modules contain overview and detailed ( ) presentation slides. Detailed slides can be hidden or removed by trainers.
  Additional slides can be customized for local conditions ( )
  Training takes about a half-day to complete
Notes: Speaker Instructions:
Trainers can select either the game-based or exercise-based track. Both are designed to take approximately 3-4 hours to complete. The training integrates a high-level powerpoint presentation with games, worksheets, exercises, and facilitated discussions, depending on the selected training track. The training is designed to be interactive and promote discussion and collaboration within and across city departments.
You may wish to edit this slide to identify the option you have selected.

## Slide 6: Climate Change Preparedness What experience do you have incorporating climate change into project planning or design?
Notes: [OPTIONAL SLIDE]
Speaker notes:
Has anyone in the room worked on projects that incorporate climate change into the planning process? What climate hazards were considered?
This is an optional slide that can be used to gauge familiarity of the participants with the process and facilitate a brief discussion among staff who may not know each other. Trainer should limit discussion to 5 minutes.

## Slide 7: Intro to Climate Change
Why does climate change matter to the City of ___________?
Notes: Speaker Instructions:
Customize for your city.

## Slide 8: Global Climate Trends
Image: IPCC 2014
A
(a)
(b)
(c)
(d)
Notes: Speaker notes:
Since the Industrial Revolution began in the mid-1800s, increased greenhouse gas emissions (such as carbon dioxide, CO2) have altered the Earth’s climate by trapping heat in the atmosphere. As global temperatures have risen, we have observed changes in global sea levels, oceanic circulation, and atmospheric weather patterns. These changing environmental conditions are carefully measured by scientists around the world.
For example, in 2013, atmospheric CO2 levels exceeded 400 parts per million (ppt) – a level not reached in the last 3.6 million years. Additionally, each of the last three decades has been increasingly warmer than the previous.
July 2016 was the hottest month ever recorded according to NASA, and 14 of the 15 hottest years have occurred since 2000.

## Slide 9: Global Climate Projections
Change in average sea level (1986-2005 to 2081-2100)
Change in average precipitation (1986-2005 to 2081-2100)
Notes: Speaker notes:
Scientists use Global Circulation Models, or GCMs, to simulate the planet’s response to future GHG emission scenarios and make projections of future temperature, precipitation, and sea level. These figures show projected changes in average precipitation and sea level for two future GHG emission scenarios at the end-of-century.
As you can see, changes will not be uniformly around the globe. Scientists and engineers analyze GCM model output to make local projections of future climate conditions to use in planning and design of projects.

## Slide 10: High Level Overview of Climate Change Trends in North America
Information adapted from NCA (2013) and IPCC AR5 (2014)
Notes: Speaker Notes:
Across North America, the climate will not change in the same way in all regions and different regions will experience different types of climate hazards, such as extreme temperatures or precipitation, wildfires, or sea level rise. The icons indicate some of the climate trends in different areas across North America. For example, the southeast may experience climate hazards related to sea level rise, extreme weather, and drying trends, whereas California may experience climate hazards related to sea level rise, wildfires, and drought.
Considering climate change trends and projections at a local level is critical to understanding how climate change might have an impact on your city.

## Slide 11: The Changing Climate – Northeast U.S. (Local Example)
Average temperatures  4.5°F – 10°F by 2080s
Increasing frequency, intensity and duration of heatwaves. 60 days over 90°F annually by 2100, compared to >10 days a year
A 5% to 20% increase in winter precipitation
Increase in the frequency of heavy downpours
Sea level rise of 2 to 6 ft by 2100 in the Boston area, above the global average of 1 to 4 ft
Notes: Speaker Notes:
[CUSTOMIZE NEXT SLIDE FOR YOUR REGION – this is an example from the Northeast US – delete if you prefer and just use your region]
Key sources of climate information include:
the National Climate Assessment, U.S. global Change Research Program (2014); http://nca2014.globalchange.gov/
The U.S. Climate Resilience Toolkit (https://toolkit.climate.gov/)
The Northeast US is projected to experience more frequent and more intense extreme events – heat, rainfall, winter storms.
Research still ongoing regarding ‘blocking’ the phenomenon of cold weather events sitting over an area like the 2014 Winter in the North East.
The frequency and duration of extreme cold events in the Northeast may be affected by potential increases in “blocking” events, described by the National Climate Assessment (NCA) as large-scale weather patterns with little or no movement. The NCA acknowledges that further research is required since conclusions about trends in “blocking” depend on the method of analysis. U.S. Global Change Research Program. (2014). 2014 National Climate Assessment. Retrieved from http://nca2014.globalchange.gov/

## Slide 12: The Changing Climate – ADD YOUR REGION
Average temperatures  x by 20XX
XXXXX frequency, intensity and duration of heatwaves. XX days over 90°F annually by 2100, compared to >XX days a year
A X% to xx% increase/decrease in winter precipitation
XXXXX in the frequency of heavy downpours
Sea level rise of x to Y ft by 2100 in the XXXXX area, above the global average of 1 to 4 ft
Notes: Speaker Notes:
[CUSTOMIZE FOR YOUR REGION – this is an example from the Northeast US]
Key sources of climate information include:
the National Climate Assessment, U.S. global Change Research Program (2014); http://nca2014.globalchange.gov/
The U.S. Climate Resilience Toolkit (https://toolkit.climate.gov/)
Other regional resources

## Slide 13: Motivation for Action
 | NEPA Requirements August 2016: release of updated guidance for Federal agencies on how to consider greenhouse gas emissions and the impacts of climate change in their NEPA analyses | Toyota lost $1.2B in product revenue after the 2011 earthquake & tsunami – 150,000 fewer Toyota autos were manufactured in USA | “Climate change isn’t an environmental issue. It’s a fundamental economic challenge for us.” U.S. EPA Chief Gina McCarthy July 31, 2013
The President
Executive Order 13653
Preparing the United States for the Impacts of Climate Change
Executive Order 13690
Federal Flood Risk Management Standard
Notes: Speaker Notes:
The very real risks presented by extreme weather events and longer term changes in the climate are recognized by many sectors.
The President has issued a directive that all agencies to look at the issue of climate change and also updated the federal flood risk management standard.
NEPA guidance considers these issues in their analysis and decision making. For Example the NEC FUTURE real EIS is considering how changes in flood risk and temperature may influence route-options and ultimately design.
Toyota experienced the impacts of extreme weather events on its supply chain in 2011. Climate change and extreme weather may also impact delivery of goods and services to cities, especially during times of natural disasters.

## Slide 14: Taking Action
 | Climate Change Risk Assessment of Electrician Distribution assets (2012-2015) Using PIEVC protocol and GIS methods to assess risks associated with multiple extreme weather events | Federal Railroad Administration: Tier 1 EIS (2014-) Considering impacts to proposed alternatives from flooding (coastal and riverine) and extreme temperatures as part of decision making process | 
City of San Francisco Sea Level Rise Action Plan (2016)
A call to action for City departments and stakeholders to work together to make San Francisco a more resilient city in the face of rising sea levels.
City of Cambridge
Climate Change Vulnerability Assessment (2015)
Focusing on vulnerabilities associated with changes in precipitation and temperatures
Notes: Speaker Notes:
Action on climate change is no longer something new and radical.
Many organizations across all sectors are taking action.
Feel free to add a regional or local action that will resonate with your staff.
Public agencies and government: San Francisco and Cambridge, MA are examples. Many towns across the US and the world have been tackling the issue.
Utilities : Many power and water utilities are working to understand the implications of climate change. This has included incorporating into rate submissions and design work. Toronto Hydro conducted a vulnerability assessment of its infrastructure. In Boston the Water and Sewer Commission has adjusted its design storms to allow for rising sea levels and increases in intensity of extreme rainfall events.
Transportation: The FHWA has funded many projects that investigated the risks of climate change and informed design and planning of assets.

## Slide 15: Flooding Processes
What are different causes of flooding?
Notes: Speaker Instructions:
The next section will present a high level discussion of some of the causes of flooding that may impact your City’s assets. This may seem obvious but experience has shown this can be a cause of misunderstanding.

## Slide 16: Overview of Flooding Processes
Coastal
Riverine
Urban
Large waves, high tides, storm surge
Large river flow caused by heavy precipitation
Heavy precipitation causing an overflow of the drainage system
Image: AP Photo/Michael Dwyer
Image: Kurtis Alexander (sfgate)
Image: NOAA NWS
Notes: OVERVIEW
Speaker Notes:
Coastal Flooding: Caused by large waves, high tides and strong winds (hurricanes) elevating the coastal water level. Large waves can break over coastal barriers (pictured). Elevated coastal water levels can exceed the elevation of the beach and flood the developed area behind the beach
Riverine Flooding: Flow of river exceeds capacity of channel and water overflows channel banks. Large river flows caused by precipitation, melting snowpack, high runoff
Urban Flooding: Heavy rains causes a backup in the stormwater drainage system of urban areas. Storm water overflows from system causing flooding in cities and urban areas. Impervious surfaces (i.e. – concrete/asphalt) cause high runoff into sewer systems.
Coastal Image Source:
http://www.livescience.com/11264-monster-waves.html
http://www.livescience.com/images/i/000/009/123/original/ig23_waves_coastal_flood_02.jpg?interpolation=lanczos-none&downsize=660:*
Credit: AP Photo/Michael Dwyer. Waves crash over the sea wall in Winthrop, Mass., Saturday, Jan. 4, 2003.
River image source:
http://www.weather.gov/dmx/preparefloodintro
http://www.weather.gov/images/dmx/Preparedness/River_Flood.jpg
Urban image source:
http://www.sfgate.com/bayarea/article/Highway-101-in-S-F-prone-to-flooding-5017807.php
Southbound Highway 101 in San Francisco, near Paul Avenue, flooded during last week's rainstorm, as witnessed in this photo shot from a car. Traffic was reduced to one or two lanes, depending on how deep drivers were willing to submerge their vehicles.
Photo: Kurtis Alexander

## Slide 17: Flooding can be Interrelated
Coastal and Urban
High tides and storm surge prevent stormwater from discharging, causing a backup of the system, resulting in stormwater overflowing into the streets.
Coastal and Riverine
A storm brings high winds resulting in storm surge and coastal flooding. Simultaneously, the same storm brings heavy precipitation, causing riverine flooding, which is exacerbated by high tides.
Image Source:
Theodore Scontras/University of Maine
Image Source: Sewer System
Improvement Program
(Urban Watershed Assessment Team 2013)
Notes: OVERVIEW
Speaker Notes:
Top panel: Example of coastal flooding contributing to urban flooding via backup of the stormwater system.
Bottom panel: Example of a coincident riverine and coastal storm impacted a coastal region.
_________________________________________________________
Coastal/urban schematic source:
Sewer System Improvement Program – Bayside Drainage Basin urban Watershed Characterization. Final Draft Technical Memorandum. Prepared for SFPUC. Prepared by Urban Watershed Assessment Team (p.2-29)
Coastal/riverine schematic source:
http://www.climatecentral.org/news/rain-storm-surge-risk-for-coast-19284
This schematic shows how the coincident occurrence of precipitation and storm surge (large enough to cause direct flooding or to slow down or fully block freshwater drainage) can lead to compound flooding in coastal regions. Credit: Theodore Scontras/University of Maine

## Slide 18: Climate Hazards and Impacts
What are the impacts of climate change?
Notes: Speaker Notes:
The next set of slides discusses climate hazards that are relevant to city assets and operations and provides an opportunity for the trainer to customize the content to reflect local climate projections.

## Slide 19: Climate Hazards and Impacts
Buildings and Property: Water damage, reduced capacity
Environmental Flooding, erosion, habitat impacts
Health and Safety Loss of power for light, pumping, communication, air conditioning; water quality, vector-borne diseases
Supply chain Disruption to transport network
Operations and finance Water damage to equipment, reduced capacity
Notes: Speaker Notes:
Climate hazards span a range of disciplines from environmental to health and safety. Climate hazards pose challenges and impacts to supply chains, operation, and finance.
  To evaluate climate hazards and impacts in your community, it is critical to have local information on the nature of those impacts.

## Slide 20: Miami Beach Example: Regional and Local Impacts
Image: National Weather Service
Image: Marsha Halper (Miami Herald)
Extreme tide events today
Image: Noor (New Republic)
Notes: TEMPLATE
Speaker Instructions:
This is an example slide of local climate impacts of king tide and precipitation flooding in Miami Beach, Florida. You can choose to delete this example and just use your own.
Miami Beach, a city just over 4 feet above sea level, is experiencing frequent flooding from storm events and, now, tidal inundation. During tidal flood events, the City activates pumps to keep seawater from overwhelming drainage systems and flooding city streets (lower right photo).
As sea levels continue to rise, these impacts will worsen in magnitude and frequency. Miami Beach is currently undertaking a sea level rise vulnerability study to better understand the impacts of sea level rise on City assets and services.

## Slide 21: Miami Beach Example: Regional and Local Sea Level Trends
Florida Sea Level Risks
Notes: TEMPLATE
Speaker Instructions:
This slide shows an example of conveying local trends in the climate hazard, sea level rise, at the City of Miami Beach. You can choose to delete this example and just use your own.
Over the past 100 years, sea levels in Southern Florida have risen by ~9 inches. As a low-lying state, Florida is especially prone to the influence of rising sea levels. Throughout geologic history, the state has fluctuated from being a large peninsula to a series of small islands.
The majority of southeast Florida is currently less than 6 feet above sea level and rising seas and groundwater levels threaten to inundate the state’s low-lying shoreline.

## Slide 22: Climate Hazards: ADD YOUR Regional and Local Trends
Add image or tables of historical local trends
Add map or image of historical local trends
Add image or tables of historical local trends
Notes: [TRAINER SHOULD UPDATE THIS SLIDE – SEE MIAMI BEACH EXAMPLE SLIDES]
Speaker notes:
Because we’ve seen that climate effects will be felt differently around the world, it’s important to tailor climate adaptation strategies based on local, not global, projections.
This slide is used to convey existing local climate hazards. Trainer should input relevant observed climate hazards here. This slide doesn’t have to be limited to sea level rise, riverine, or urban flooding but may include other hazards as well.

## Slide 23: Climate Impacts: ADD YOUR Regional and Local Impacts
Add image of existing impacts from climate stressor
Add image of existing impacts from climate stressor
Add image of existing impacts from climate stressor
Notes: [TRAINER SHOULD UPDATE THIS SLIDE – SEE MIAMI BEACH EXAMPLE SLIDES]
Speaker notes:
Because we’ve seen that climate effects will be felt differently around the world, it’s important to tailor climate adaptation strategies based on local, not global, projections.
This slide is used to convey existing local climate impacts. Trainer should input relevant observed climate impacts here. An example photo could also be included of the hazard’s impact.
This slide doesn’t have to be limited to sea level rise, riverine, or urban flooding but may include other hazards as well.

## Slide 24: Climate Impacts Regional and Local Impacts (Optional) What are the important flooding sources in our community? What assets or operations are impacted during flood events?
Notes: [OPTIONAL SLIDE]
Speaker notes:
This is an optional slide that can be used to facilitate discussion about your city’s flooding sources and impacts of flooding. Trainer should limit discussion to 5 minutes.

## Slide 25
Climate Hazards and Impacts Applicable Case Studies:
Capital Regional District Coastal Sea Level Rise Risk Assessment
Baltimore Preparedness & Resiliency Disaster Preparedness Project & Plan
Notes: Climate Change Projections

## Slide 26: Cascading Impacts Exercise (Optional)
Exercise Track: Do Cascading Impacts exercise
Game of Floods track:
Skip exercise
Notes: Speaker Instructions:
This is an optional exercise that is targeted at the exercise-based track but could be used for the game track. However, it is recommended that it is only used for the exercise-based track in order to keep to the 3.5 hour training time.
You should allow a maximum of 20 minutes for this exercise.
See How to guide for more instructions.

## Slide 27: Cascading Impacts Exercise (Optional)
Using the provided worksheet, for one climate stressor identify the cascading impacts that will affect your job / service / particular asset type
‘Cascade’ those impacts outwards from the center of the circle
Impacts can flow sideways as well as outwards
Identify physical, social and economic impacts that overlap between different services / departments
Notes: Speaker Instructions:
This is an optional exercise that is targeted at the exercise-based track but could be used for the game track. However, it is recommended that it is only used for the exercise-based track in order to keep to the 3.5 hour training time.
You should allow 20 minutes for this exercise.
See How to guide for more instructions.

## Slide 28: Cascading Impacts Exercise (Optional)
Table No.: __________
Facilitator:__________
Principal Stakeholders that need to collaborate:
1)
2)
3)
Assets already affected by climate stressor
1)
2)
3)
Watershed
flooding
Notes: Speaker Instructions:
This is an optional exercise that is targeted at the exercise-based track but could be used for the game track. However, it is recommended that it is only used for the exercise-based track in order to keep to the 3.5 hour training time.
See How to guide for more instructions.
This is an example worksheet that can be printed out for each group doing the exercise. A different hazard can be placed in the center of the circle.

## Slide 29: Cascading Impacts Exercise (Optional)
Notes: Speaker Instructions:
This is a photograph of a filled in worksheet.
See How to guide for more instructions.

## Slide 30: Process for Incorporating Climate Change into Project Planning
1
2
3
6
5
4
Review Science
Inventory Assets and Operations
Assess Risk
Plan Adaptation
Implement Adaptation Measures
Monitor
Assess
Vulnerability
Stakeholder Engagement
Adaptive
Capacity & Thresholds
Physical Governance Information
Likelihood Consequence Prioritization
Exposure
Sensitivity
Adaptive
Capacity
Function Location Condition
Identify
climate scenarios
Adopt Construct
7
Notes: Speaker Notes:
This is the adaptation planning process which is commonly followed by cities and other organizations. It has 7 main steps. Although cities should start at Step 1 (Review Science) in the cycle, many of the actions will be ongoing and/or will need to be revisited on a regular basis. Many cities are at Step 3 and 4 of the process , although some may already have some asset or neighborhood-specific plans in place to tackle areas that are already at risk of frequent flooding. Stakeholder engagement is at the center of the process, indicating the need to engage with city staff, asset managers, resource agencies, and permitting agencies along the way. The subsequent slides walk through each of these steps in more detail.

## Slide 31: Review Climate Science
How do we identify and select local climate change projections?
Notes: Speaker Notes:
The next set of slides discusses how to approach selections of relevant local climate change projections for planning, design, and operations.

## Slide 32: Step 1 – Review the Science
1
2
3
6
5
4
Review Science
Inventory Assets and Operations
Assess Risk
Plan Adaptation
Implement Adaptation Measures
Monitor
Assess
Vulnerability
Stakeholder Engagement
Adaptive
Capacity & Thresholds
Physical Governance Information
Likelihood Consequence Prioritization
Exposure
Sensitivity
Adaptive
Capacity
Function Location Condition
Identify
climate scenarios
Adopt Construct
7
Notes: Speaker Notes:
The first step in the climate adaptation process is developing an understanding of the climate science and future projections that are relevant to your city.

## Slide 33: Step 1 – Review the Science
Establish scientific basis for climate change projections
Consider climate variables relevant to location
Select appropriate projections and planning horizons
Notes: OVERVIEW
Speaker notes:
Preparing for climate change begins with an understanding of the current state-of-the-science. It is necessary to establish the scientific basis upon which to draw climate change projections. Having a solid scientific foundation for your climate change projections will increase the credibility of your assessment and increase stakeholder buy-in into the process.
After identifying the best sources of climate change science, it is necessary to identify the climate variables of interest for your region and assets. For example, stormwater infrastructure may be vulnerable to sea level rise and changes in precipitation intensity, whereas water supply/snowpack may be vulnerable to changes in annual precipitation amounts, changes in the fraction of precipitation falling as snowfall vs. rainfall, and longer term cycles of drought.
The final step is the selection of appropriate climate change projections and planning horizons. Planning horizons for climate projections are often aligned with a City’s planning process, which may only look out 10 to 30 years into the future; however, it is important to consider the long-term viability of critical city assets and services farther out into the future in some cases. Some cities evaluate climate change impacts to critical infrastructure with functional life spans of 75 to 100 years and therefore may consider climate change projections as far out as 2100. Others may require design of infrastructure to accommodate expected changes out to 2050 but incorporate into the design the ability to adapt that infrastructure for future conditions beyond 2050.

## Slide 34: Step 1 – Review the Science
Establish scientific basis for climate change projections
City guidance
Regional compacts
Academic institutions
Sources for Climate Change Projections
Notes: DETAIL
Speaker Notes:
There are many places to get up-to-date climate science projections relevant to your community. The first place to look is at the local, city level. Many cities (such as San Francisco and Seattle) have started to develop guidance documents to ensure future planning across all departments is based on consistent projections.
If city-level data is unavailable, some larger-scale areas that share a similar climate have developed regional compacts to form a collaborative effort of climate resilience at a regional scale (Southeast Florida Regional Compact and NRC 2012, which provides sea level projections for the west coast of the U.S.).
If city or regional information has not yet been created for your area, local academic institutions are also a great place to partner with for local climate projections. They are often involved in research to advance climate science at a local level. For example, grant funding secured by the city of Portsmouth, New Hampshire was used to commission a study by experts at the University of New Hampshire and the Rockingham County Regional Planning Commission to calculate local sea level rise rates that were used in the Portsmouth 2015 Master Plan to prioritize capital projects.
Many universities have also established collaboratives that serve as a shared information hub (LA Regional Collaborative established by UCLA; Capital Region Climate Readiness Collaborative established at the University of California, Davis)

## Slide 35: Step 1 – Review the Science
Consider climate variables relevant to location
Local Assets
Temperature
Sea Level Rise
Precipitation
Drought
Extreme Weather
What climate variables are relevant to your region?
Notes: DETAIL
Speaker Notes:
It is important to select climate hazards that that are relevant to the assets of concern. Most communities will likely need to assess the impacts of multiple climate hazards in their vulnerability studies, although it is fine to initially focus on a single climate hazard or asset category (such as stormwater or transportation infrastructure) to make the assessment more manageable.

## Slide 36: Step 1 – Review the Science
Climate Change Scenario Selection
Risk Tolerance
Asset Lifespan
Consistency
Selected Projections and Planning Horizons
Notes: DETAIL
Speaker Notes:
During project planning, selection of appropriate climate change projections for assets can be challenging. There are several factors that influence selection of climate projections and planning horizons:
Functional lifespan – How long will the project be in use at this location (is project located in hazard zone during lifespan)? It is important to identify in what year the asset will be constructed and plan forward from that baseline.
Risk tolerance – Managers may choose to plan now for the high end of the uncertainty range (particularly for critical assets or assets which are not easily adapted in the future). Some water-dependent assets such as boardwalks or promenades, by their nature, will be built in close proximity to the water and may be exposed to infrequent flooding from time to time. Because inundation of these assets is relatively low risk, it may not be necessary to elevate these assets to accommodate the high-range of future projections if they are designed in such as way that they are not adversely impacted by temporary flooding. For most assets, it may be appropriate to plan for a mid-range scenario while completing sensitivity testing and developing adaptation strategies to implement in the future to accommodate higher range projections if they occur.
Consistency – Are the scenarios consistent between city departments, external agencies, and local legislative requirements?

## Slide 37: Climate Change Projections
What should we be planning for?
Notes: Speaker Notes:
The next set of slides provides an opportunity for the trainer to provide participants information regarding local climate change projections for your city.

## Slide 38: Select appropriate scenarios and time horizons Example: Southeast Florida Compact
Critical
Infrastructure (non-adaptable)
Short-term
Mid-term
(adaptable)
Notes: [TEMPLATE]
Speaker Notes:
This is an example of sea level rise projections for the southeast Florida region. The selected sea level rise curve depends on the asset characteristics and anticipated functional life span.
Short-term infrastructure: low risk projects that are easily replaceable with short design lives (less than 50 years), are adaptable and have limited interdependencies with other infrastructure or service
Mid-term infrastructure: moderate risk projects that are adaptable and have minimal interdependencies with other infrastructure or service
Critical Infrastructure: high risk projects to be constructed after 2060 or projects which are not easily replaceable or removable, have a long design life (more than 50 years) or are critically interdependent with other infrastructure or services

## Slide 39: Climate Hazards: Local Sea Level Rise, New York City
Baseline (2000-2004) | Low (inches) | Middle (inches) | High (inches)
2020 | 2 | 4 to 8 | 10
2050 | 8 | 11 to 21 | 30
2080 | 13 | 18 to 39 | 58
2100 | 15 | 22 to 50 | 75
Image: Flickr user Chris Ford
Notes: [TEMPLATE]
Speaker notes:
This is an example of local sea level rise estimates relevant to New York City (based on the New York State Energy Research & Development Authority 2014 study). By applying the projected changes (based on GCM output) to observed data, the projections become specific to the region. High, moderate, and low sea level rise projections are given for key planning time periods throughout the coming century.

## Slide 40: Climate Hazards: Local Precipitation, New York City
Baseline (1971-2000) 49.7 inches | Low (% increase) | Middle (% increase) | High (% increase)
2020 | - 1 | +1 to +8 | +10
2050 | +1 | +4 to +11 | +13
2080 | +2 | +5 to +13 | +19
2100 | +6 | -1 to +19 | +25
Image: Flickr user Erin Johnson
Notes: [TEMPLATE]
Speaker notes:
This is an example of local changes in precipitation estimates relevant to New York City (NYSERDA 2014). By applying the projected changes (based on GCM output) to observed data, the projections become specific to the region. High, moderate, and low sea level rise projections are given for key planning time periods throughout the coming century. Although seasonal projections are less certain than annual results, much of the additional precipitation is projected to occur in the winter months. During late summer and early fall, total precipitation is slightly reduced in many climate models. In general, there projected changes in annual precipitation associated with GHG increases are small relative to year-to-year variability.

## Slide 41: Climate Hazards: ADD YOUR Local Sea Level Rise/Precipitation Projections
Baseline (2000-2004) | Low (inches) | Middle Range (inches) | High (inches)
2020 |  |  | 
2050 |  |  | 
2080 |  |  | 
2100 |  |  | 
Add Picture Here
Add local climate
hazard information
here
Add relevant
planning horizons
here
Notes: [TRAINER SHOULD UPDATE THIS SLIDE – SEE NEW YORK CITY EXAMPLE SLIDES]
Speaker notes:
Because we’ve seen that climate effects will be felt differently around the world, it’s important to tailor climate adaptation strategies based on local, not global, projections.
This slide is used to convey projected local climate hazards. Trainer should input relevant time frames and projected local stressor changes in the table as shown. An example photo should also be included of the stressor’s impact.
This slide is not limited to sea level rise, but may include other hazards as well.

## Slide 42
Climate Change Projections Applicable Case Studies:
Berkeley Watershed Modelling and Climate Change Masterplan
Baltimore Preparedness & Resiliency Disaster Preparedness Project & Plan
Notes: Climate Change Projections

## Slide 43: Climate Science Exercise
Exercise Track: Do thought exercise in Climate Science Section of Exercise Workbook
Game of Floods Track:
Distribute game board, roles, budget, and assigned climate scenario card to each team
Notes: Speaker Instructions:
For the exercise-based track, have participants complete the climate science section in the Exercise workbook.
Game-based track:
Distribute Game of Floods game board, budget, and climate scenario to each team.
Assign “role cards” to each participant.
Briefly introduce background of Resilience Harbor and orient participants on flood sources and various asset types.
Time: Allow 5-10 minutes.

## Slide 44: Asset and Operations Inventory
What are our critical assets and how are they impacted by climate hazards?
Notes: Speaker Notes:
The next section will discuss how to identify and prioritize assets for consideration in a vulnerability and risk assessment, including developing an understanding of what aspects of a given asset contribute to its sensitivity to climate hazards.

## Slide 45: Process for Incorporating Climate Change into Project Planning - Step 2
1
2
3
6
5
4
Review Science
Inventory Assets and Operations
Assess Risk
Plan Adaptation
Implement Adaptation Measures
Monitor
Assess
Vulnerability
Stakeholder Engagement
Adaptive
Capacity & Thresholds
Physical Governance Information
Likelihood Consequence Prioritization
Exposure
Sensitivity
Adaptive
Capacity
Function Location Condition
Identify
climate scenarios
Adopt Construct
7
Notes: Speaker Notes:
The asset and operations inventory step identifies and collects the relevant asset information required to conduct the vulnerability and risk assessment. The asset and operations inventory can begin concurrently with Step 1 and focuses on collecting information pertinent to an asset’s function, location, and condition. All of these factors contribute to an asset’s sensitivity to climate hazards such as extreme heat or temporary flooding.

## Slide 46: Asset and Operations Inventory
What categories of assets should be considered (transportation, stormwater, parks, etc.)?
Within each category, which assets are most critical to city operations?
What non-critical assets are important to the city and its residents?
What data and information do we have?
Is there a database or GIS data layers?
If not, how can we obtain the required information?
What subset of assets will be carried forward to the vulnerability assessment?
ASSET INVENTORY
Identify Categories + Individual Assets
Meet with managers and stakeholders; collect data, identify gaps
ASSET SELECTION
Select unique and representative assets
Notes: OVERVIEW
Speaker Notes:
This graphic shows an overview of the asset inventory process, where a range of assets is initially identified and subsequently only specific assets are identified for further evaluation in the vulnerability assessment. This process can be applicable for cities/systems with many assets and asset types and helps focus the data collection process on key assets.
The first step is to inventory the City’s assets and organize the assets into asset categories, such as stormwater, wastewater, transportation, parks, etc.. Then through meetings with city staff and asset managers, critical assets are identified, potential data sources are gathered, and data gaps are identified. Finally, both unique and representative assets may be identified to carry forward to the vulnerability assessment. It is not typically practical or beneficial to try to examine every single asset in the vulnerability assessment or in the development of adaptation solutions. Some prior studies have gone the route of selecting representative assets within each asset category for detailed evaluation.
The asset and operations inventory can be an iterative process that requires input from multiple groups to identify the most relevant assets types that may be exposed to the climate hazard of interest. Collected data may be in either geospatial or tabular format, including survey data, historical accounts, institutional knowledge, or GIS layers. Data gaps may dictate the level of analysis that is possible for the vulnerability assessment, as some cities may not have all the required data for a rigorous assessment.

## Slide 47: Asset and Operations Inventory Example Asset Characteristics
Location and elevation*
Age and materials
Condition, operations and maintenance costs, prior performance
Criticality
Ownership
Repair time and cost to replace
Design criteria and level of service
Level of use (ridership, car/truck trips, etc..)
*Adjacent ground, finish floor, or mechanical, electrical, plumbing (MEP) elevations
Notes: OVERVIEW
Speaker Notes:
This slide provides examples of the types of asset characteristics that may be collected during the asset and operations inventory.
Much of this data may already exist in the form of as-built drawings, existing studies, operations and maintenance reports, or other routine condition assessments. In many cases, this information may have already been collected by an existing department within your city. Therefore it is beneficial to maintain a channel of communication between all relevant departments throughout the during and after the vulnerability study.

## Slide 48: Asset and Operations Inventory Considerations for Sensitivity
What makes an asset sensitive to flooding?
Asset sensitivity is difficult to quantify
Studies typically adopt “indicators” of sensitivity, such as:
Asset condition (age, materials, etc.)
Level of use (average daily traffic, discharge, capacity, etc.)
Prior climate impacts (flooding, extreme heat, etc.)
Susceptibility to flood impacts (flood-proofed, corrosion resistant, backflow prevention)
Socio-economic factors (asset serves vulnerable or disadvantaged populations)
Flood barrier, Fargo, ND
Source: Flood Control America, LLC; FEMA (2013)
Flood-proofed generator door
Source: FEMA (2013)
Notes: OVERVIEW
Speaker Notes:
This slide shows key asset characteristics that contribute to an asset’s sensitivity to climate hazards. Sensitivity is one aspect of vulnerability that is evaluated as part of an vulnerability assessment. Because sensitivity is difficult to quantify, studies typically identify several key sensitivity “indicators” which are then rated in a relative sense to evaluate the sensitivity of one asset vs. another. Example possible sensitivity indicators are listed in this slide – for example, the age of the asset, whether or not it is flood-proofed, or if it serves socio-economically disadvantaged populations.

## Slide 49: Asset and Operations Inventory Considerations for Adaptive Capacity
Redundancy (e.g., back-up generator)
Availability of alternate routes
Potential for maintaining partial use while flooded
Potential to increase elevation in future (e.g., elevate building, install seawall extension or cap)
Identify thresholds for impact (timing of impacts and future adaptation)
Identify barriers to adaptation (e.g., site or policy constraints)
Source: americantrails.org
Seawall
extension
Notes: OVERVIEW
Speaker Notes:
This slide shows key asset characteristics that may be considered when evaluating the adaptive capacity of an asset. Adaptive capacity is one aspect of vulnerability that is evaluated as part of an vulnerability assessment. Asset characteristics such as redundant systems or routes or potential barriers to future modification to adapt to climate change should be noted during the data collection process.

## Slide 50: Asset and Operations Inventory Transportation Asset Categories
Asset Type | Examples | Sensitivity to Flooding | Data Needed
Surface transportation | Roads, bridges, rails, | Loss of function while flooded, but may recover afterwards. Rails can be more sensitive if they require electricity to operate (power supply and control systems). Physical damage from flood forces. | Elevations of key components; operational thresholds (depth of flooding)
Transit hubs | Airports, rail stations, ports | Comprised of many assets (e.g., buildings and roads). Performance during flooding can be governed by most sensitive (or lowest elevation) component (e.g., power supply, road or rail access). | Elevations of key components
Notes: DETAILED
Speaker Notes:
Here are some examples of major asset categories, and how some of these assets are sensitive to flooding. As the individual assets of each system are unique, this graphic provides an generalized overview that may be applicable to a wide range of cities and systems.

## Slide 51: Asset and Operations Inventory Transportation Asset Sensitivity Local Assets (from YOUR CITY)
 | Asset | Sensitivity to Flooding
Transportation |  | 
Notes: DETAILED
Speaker Instructions:
Template to fill out specific to Trainer’s city/system. Identify city assets and brainstorm characteristics of each asset that may make it sensitive to flooding.
Example assets: bridges and tunnels, roads, rail, transit system, port and airport, back-up power and communications, evacuation routes, intelligent transportation systems
Example sensitivities: structural damage from coastal storms, temporary closure during flood events, damage to electrical components, loss of access

## Slide 52: Asset and Operations Inventory Stormwater Asset Categories
Asset Type | Examples | Sensitivity to Flooding | Example Data Needed
Buildings | Pump stations, treatment facilities, operation centers | Physical damage from flooding. Electrical and power components sensitive to water, and typically located below grade, or on the first floor Entrances (e.g., doorways and windows) allow water to reach inside buildings | Lowest adjacent grade; elevations of key components (e.g., electrical panels, doorways, pump motors)
Storm and wastewater infrastructure | Buried pipes, culverts, detention/ retention basins, outfalls | Ability to withstand flooding. Climate change may result in impacts to capacity and level of service of overall system. Outfalls that cannot discharge during higher tides will impact the performance of the entire system. | Invert elevations of outfalls, storage basin elevations
Notes: DETAILED
Speaker Notes:
Here are some examples of major asset categories, and how some of these assets are sensitive to flooding. As the individual assets of each system are unique, this graphic provides an generalized overview that may be applicable to a wide range of cities and systems.

## Slide 53: Asset and Operations Inventory Stormwater Asset Sensitivity Local Assets (from YOUR CITY)
 | Asset | Sensitivity to Flooding
Stormwater |  | 
Notes: DETAILED
Speaker Notes:
Template to fill out specific to Trainer’s city/system. Identify city assets and brainstorm characteristics of each asset that may make it sensitive to flooding.
Example assets: storm sewer network (sewers, culverts, detention basins); pump stations; water treatment facilities; outfalls
Example sensitivities: increased flooding may exceed capacity, flooding of water-sensitive electrical components, infiltration by high tides or elevated groundwater levels

## Slide 54: Asset and Operations Inventory Asset Elevation Information (Template)
Electrical panels
Fuel tanks
Sump pumps
Flooding points:
      Vents
      Windows
      Door entrances
      Floor hatches
      Conduits
Image source:
Retrofitting Buildings for Flood Risk (Coastal Climate Resiliency – NYC Planning , 2014)
Notes: DETAILED [TEMPLATE]
Speaker Instructions:
Here is example of asset details to think about when collecting asset information for building structures. This is common across many systems, but may be customized per individual system.
Flooding can impact building structures both outside and inside. While building themselves may recover post-flooding, many of the components inside a building may not. There are several pathways water can take into a building during storm events.
Image source: Retrofitting Buildings for Flood Risk (Coastal Climate Resiliency – NYC Planning 2014)
Image source http://cdn1.facilityexecutive.com/wp-content/uploads/2016/01/SGH_flood_figure2.png

## Slide 55: Asset and Operations Inventory Asset Elevation Information (Template)
..
..
…
….
Add image or drawing of example asset
Notes: DETAILED [CUSTOMIZE]
Speaker Instructions:
Template to fill out specific to Trainer’s city/system. Pick an example asset and try to identify the characteristics shown on the previous slide.

## Slide 56: Asset Inventory Exercise – 1 of 2
Game track: Complete asset inventory table in Workbook for Game of Floods (see next slide for instructions)
Exercise track:
Complete asset inventory exercise in the Participant Exercise Workbook
Notes: Speaker Instructions:
For the game-based track, have participants complete the asset inventory table in the Game of Floods participant workbook and follow the steps provided on the next slide.
For the exercise-based track, have participants complete the asset inventory table in the Exercise workbook.

## Slide 57: Asset Inventory Exercise – 2 of 2
Review the game board and identify assets.
Consult with your team and select assets for further evaluation.
Consider your assigned role when selecting assets.
Assemble list of assets that should be considered in Climate Change Adaptation Plan.
Facilitators will provide each team with Asset Cards describing each asset.
Complete the Asset Inventory Table using information from the Game Board and the Asset Cards.
Notes: Speaker Instructions:
For the game-based track, have participants complete the asset inventory table in the Game of Floods participant workbook and follow the steps provided on this slide.
Time: Allow 15 minutes
For the exercise-based track, trainers can delete this slide.
Game-based track:
Distribute all asset condition cards to teams
Teams will select 9 assets they agree are important to consider for climate adaptation planning

## Slide 58
Asset and Operations Inventory Applicable Case Studies:
Adapting to Rising Tides
Capital Regional District Coastal Sea Level Rise Risk Assessment
FHWA Post Sandy Study
Notes: Asset and Operations Inventory

## Slide 59: Assess Vulnerability
How do we identify our most vulnerable assets?
Notes: Speaker Instructions:
The next set of slides will provide a high-level overview of the factors that contribute to climate change vulnerability and how asset vulnerability is evaluated.

## Slide 60: Process for Incorporating Climate Change into Project Planning - Step 3
1
2
3
6
5
4
Review Science
Inventory Assets and Operations
Assess Risk
Plan Adaptation
Implement Adaptation Measures
Monitor
Assess
Vulnerability
Stakeholder Engagement
Adaptive
Capacity & Thresholds
Physical Governance Information
Likelihood Consequence Prioritization
Exposure
Sensitivity
Adaptive
Capacity
Function Location Condition
Identify
climate scenarios
Adopt Construct
7
Notes: Speaker Notes:
The third step in the process for incorporating climate change into project planning is to assess the vulnerability of your City’s selected assets. Vulnerability is a function of exposure, sensitivity, and adaptive capacity. These three factors will be discussed in the next slides. Note that sensitivity has already be discussed to some extent as part of the asset inventory section.

## Slide 61
Vulnerability Assessment
Assess Vulnerability
Exposure
Sensitivity
Adaptive
Capacity
4
Assess Risk
Likelihood Consequence Prioritization
3
yes
yes
no
no
Is asset flooded?
(exposed)
Is asset sensitive?
Does the asset have adaptive capability?
Asset no longer part of analysis
Consider how this can help with adaptation strategies
Three step process to help PRIORITZE assets for adaptation
yes
yes
no
Notes: Speaker Notes:
Asset vulnerability is assessed in three stages by evaluating each component of vulnerability. The vulnerability assessment starts with a pool of assets to evaluate. It is generally not possible, nor useful, to consider every single asset across all asset categories (for example, stormwater infrastructure, public transportation, parks, etc.). A high-level vulnerability assessment may consider a subset of critical assets within each asset category. A detailed vulnerability assessment may focus on a single asset type within a given asset category (such as stormwater pump stations) and provide a much more detailed assessment of vulnerability. The goals and scope (department vs. city-wide) of the vulnerability assessment will inform the selection of assets for evaluation. In some cases, the pool of assets can be narrowed down through city staff and stakeholder input to focus the vulnerability assessment on critical or high priority assets (such as those currently in planning or design), as discussed previously.
Once the assets are selected, the exposure, sensitivity, and adaptive capacity are evaluated for each asset or asset category.

## Slide 62
Vulnerability Assessment: EXPOSURE
Assess Vulnerability
Exposure
Sensitivity
Adaptive
Capacity
4
Assess Risk
Likelihood Consequence Prioritization
3
yes
yes
no
no
yes
Is asset flooded?
(exposed)
Is asset sensitive?
Does the asset have adaptive capability?
Consider how this can help with adaptation strategies
Exposure: the nature and degree to which climate threats physically
touch the asset
yes
no
Asset no longer part of analysis
Notes: Speaker Notes:
The first component of vulnerability is exposure. In the example shown here, exposure to flooding is being evaluated. Exposure to other climate stressors could also be evaluated within this same framework – for example, exposure to extreme heat or urban flooding. The exposure assessment evaluates whether or not a given asset is exposed to the climate hazard. Often, this assessment is performed using GIS data layers by overlaying a map, such as an inundation map, with the asset locations. A given asset could be identified as exposed to the climate hazard (such as high tide inundation with 12 inches of SLR) if the inundation area touches the footprint of the asset, or if you have asset elevation data, if the future water level exceeds the elevation of a pump station control panel or finish floor elevation of a building, etc.. An asset exposure inventory may be developed for many or all of your assets as a first cut at vulnerability, but you will likely have to focus in on a subset of critical assets as you move to the sensitivity evaluation.
Questions asked during the sensitivity assessment could be:
Is the asset flooded?
If yes, by how much or how frequently?
How deep is the water during flood events?

## Slide 63
Vulnerability Assessment: SENSITIVITY
Assess Vulnerability
Exposure
Sensitivity
Adaptive
Capacity
4
Assess Risk
Likelihood Consequence Prioritization
3
yes
yes
no
no
yes
Is asset flooded?
(exposed)
Is asset sensitive?
Does the asset have adaptive capability?
Consider how this can help with adaptation strategies
Sensitivity: the degree to which an asset is affected
yes
no
Asset no longer part of analysis
Notes: Speaker Notes:
The second component of vulnerability is sensitivity. In the example shown here, sensitivity to flooding is being evaluated. Sensitivity to other climate stressors could also be evaluated within this same framework. The sensitivity assessment evaluates whether or not a given asset is sensitive to the climate hazard. Sensitivity is typically only evaluated for assets which are exposed to the climate hazard of interest. If an asset is not exposed to flooding, then it is not necessary to evaluate its sensitivity. This helps focus efforts on the most vulnerable assets because evaluating sensitivity is a data-driven process and collecting those data can be time consuming.
Questions asked during the exposure assessment could be:
If the asset is flooded, does it matter?
Is the asset designed to accommodate some degree of flooding or will it be damaged if it gets wet?
Does the asset recover quickly after flooding (such as an elevated roadway) or will it be out of service following the storm (such as an underpass or a pump station with below grade electrical equipment).

## Slide 64
Vulnerability Assessment: ADAPTIVE CAPACITY
Assess Vulnerability
Exposure
Sensitivity
Adaptive
Capacity
4
Assess Risk
Likelihood Consequence Prioritization
3
yes
yes
yes
no
no
no
yes
Is asset flooded?
(exposed)
Is asset sensitive?
Consider how this can help with adaptation strategies
Adaptive Capacity: the capacity of a system to accommodate stress, and/or redundancy which allows for continued functionality while impacted.
Does the asset have adaptive capability?
Asset no longer part of analysis
Notes: Speaker Notes:
The third component of vulnerability is adaptive capacity. In the example shown here, adaptive capacity to flooding is being evaluated. Adaptive capacity to other climate stressors could also be evaluated within this same framework. The adaptive capacity assessment evaluates whether or not a given asset has the capacity to accommodate a climate impact and/or has redundancy to allow for continued operations during or after a flood event. Adaptive capacity is typically only evaluated for assets which are exposed and sensitive to the climate hazard of interest.
Questions asked during the adaptive capacity assessment could be:
Does the asset have adaptive capacity?
If the asset is taken out of service, is there another nearby asset that can handle the load until the damaged asset is repaired (is there redundancy)? Sometimes an asset may have partial redundancy – for example, a bus could be used in place of a commuter railway if the railway is out of service.
Note that assets with low adaptive capacity receive a higher vulnerability score than assets with high adaptive capacity.

## Slide 65: Assessing Exposure
Exposure is one component of vulnerability – what tools can we use to characterize exposure?
Notes: Speaker Instructions:
The next set of slides provide information on using maps (inundation maps) to assess exposure of assets to flooding. The first few slides are high level overview slides and the subsequent slides provide more information for cities that may wish to create their own riverine or coastal flooding and inundation maps as part of a climate change vulnerability assessment. Note that these examples may show exposure to sea level rise; however, riverine or urban flood maps can be used in the same way to assess exposure.

## Slide 66: Exposure Maps
Temperature
Sea Level Rise
Riverine flooding
Urban flooding
Assets
Notes: OVERVIEW
Speaker Notes:
An exposure analysis identifies which assets will be exposed to a specific climate impact or hazard. It provides insight into the amount of possible damage or loss that could occur, for example to different types of transportation assets or storm sewer assets.
Readily available data and information is then used to evaluate exposure. For sea level rise the exposure analysis can answer the following questions:
Will the asset in question be exposed to inundation or flooding?
If so, during what storm event, or with what amount of sea level rise?
And, to what extent or depth with the flooding occur?
An exposure assessment requires translating the information collected during the asset inventory into a usable format. For example, using Geographic Information System software (e.g., ESRI’s ArcMap), you can overlay and intersect climate stressor data with locations of assets. Elevation data from a topographic survey, or in GIS commonly a Digital Elevation Model (DEM) is used to asses the magnitude of exposure.
Subsequent slides will focus on exposure to flooding and tools to perform that assessment.

## Slide 67: Exposure: Inundation and Flooding Maps
Exposure is one aspect of vulnerability
Maps help visualize and quantify exposure
Show shoreline “weak links” and flooding pathways
Overlay assets with inundation layer
Assess for each asset for each scenario:
  Is it inundated?
  Depth of inundation
Image source: Sea Change Boston (Sasaki Associates 2016)
Notes: OVERVIEW
Speaker Notes:
Exposure is just one aspect of vulnerability (remember vulnerability also incorporates sensitivity and adaptation capacity of assets), but it is a key piece. Exposure maps show you where assets are located relative to climate hazards, and help you quantify level of exposure. They can also show the timing of large scale inundation, which will inform the scale and timing of adaptation strategies.
Exposure maps also show you where shoreline vulnerabilities that lead to inland exposure may exist. For example, inundation maps show you where water can overtop shorelines and the pathway that water can take to reach an asset. It can also be helpful to note for each asset whether it is located immediately adjacent to water or if it is located inland and protected by flood protection infrastructure (such as a levee or seawall) along the shoreline.
The graphic shows an example of an exposure map that shows transportation assets relative to sea level rise and storm surge that could occur in Boston in 2050.
Image source: Sea Change Boston (Sasaki Associates 2016)

## Slide 68: Exposure: Inundation and Flooding Maps Level of Detail and Options
Single map, multiple scenarios
Extent of inundation (no depth)
Depicts increasing vulnerabilities and timing of impacts
Multiple maps, single scenario
Extent and depth of inundation
Identify depth of flooding at asset
Visualize low elevation areas
Identify depth of overtopping at shoreline
Top image: New York City Panel on Climate Change 2015.
Bottom image: NOAA Sea Level Rise and Coastal Flooding Impacts 2016
Notes: OVERVIEW
Speaker Notes:
Exposure maps can show various levels of detail, depending on the goals of the assessment.
Exposure maps can show multiple scenarios on a single map, so that the increase/decrease in hazard can be easily visualized. However, these maps have a tradeoff, for example depth of flooding information cannot be easily shown when multiple scenarios are overlaid together.
Depth of flood information can more easily be shown if a single scenario is shown on a single map. This can be helpful to understand the magnitude of flooding occur at an asset (is it 1 foot, or 5 feet of flooding?). However, this method requires multiple maps to be produced, which can require a larger effort and more specialized GIS/mapping expertise.

## Slide 69: Example: SLR Inundation Mapping
50-year tide
(2% Annual Chance SWEL)
High Tide at current conditions
High Tide with 24’’ SLR
High Tide with 36’’ SLR
Depth (ft)
Notes: EXAMPLE / TEMPLATE
Speaker Instructions:
This slide shows a series of sea level rise inundation maps from San Francisco Bay. This is an example that can be replaced using coastal, riverine, or urban flood maps from your city.

## Slide 70: Exposure: ADD YOUR CITY SLR MAPS
Notes: Speaker Instructions:
If your city has already done SLR, riverine, or urban flood mapping, insert examples into the deck here.

## Slide 71: Exposure: Inundation and Flooding Maps Visualization Tools
Image sources: NOAA Sea Level Rise and Coastal Flooding Impacts 2016
Notes: DETAILED
Speaker Notes:
Example of single scenarios on single maps. Depth of flooding information can be displayed along with visualization tools, such as these from NOAA, to convey on-the-ground flooding conditions to policy makers and the public.

## Slide 72: Exposure: Inundation and Flooding Maps Shoreline Overtopping Maps
  Shows potential depth of overtopping along shoreline
  Shows vulnerable locations for further assessment
  Shows shoreline segments that allow water to flood inland
  Requires GIS delineation of shoreline crest
Image source: Sea Level Rise and Overtopping Analysis for San Mateo County’s Bayshore (AECOM, 2016)
Notes: DETAILED
Speaker Notes:
Other types of information can be displayed on exposure maps, include shoreline overtopping information. This type of information can easily show a shoreline segment that may be allowing water to inundate a specific inland location. This information can also help identify where additional field investigations or complex modeling is necessary to better understand how certain areas are vulnerable.
Showing overtopping potential depth requires the crest of the shoreline to be traced.

## Slide 73: Exposure: Inundation and Flooding Maps Shoreline Delineation
Shoreline Delineation
  Shows type or use of shoreline
  Better understanding of shoreline features that affect flooding
  GIS delineation of shoreline crest
Image sources: Adapting to Rising Tides: Contra Costa County SLR Vulnerability Assessment (AECOM 2016)
v
Notes: DETAILED
Speaker Notes:
A shoreline delineation can also provide additional information as to the type of use for each shoreline segment (whether is it a engineered levee, or non-engineered berm). This can be helpful to identify the type of features that are protecting inland areas.

## Slide 74: Exposure: Coastal Inundation Maps Example Resources
Geography | Resource | Scenarios / Time Horizons | Tools
National Resources | Climate Central – Surging Seas Viewer | SLR, storm surge, tsunamis 2020 - 2100 | Maps, composite scenarios, inundation exposure analysis (overlay with societal information), summary reports
 | NOAA Sea Level Rise and Coastal Flooding Impacts Viewer | SLR above MHHW only No time horizons | Maps, exposure analysis (overlay with societal information), flood frequency graphs, street view renderings to visualize inundation depth
 | Nature Conservancy Coastal Resilience Viewer | SLR, wave run-up Current, 2030, 2060, 2100 | Maps, exposure analysis (overlay with societal information), summary reports
Regional Resources | California Coast Our Coast Our Future | SLR and storm surge 2020 - 2100 | Maps, exposure analysis, scenario comparisons
 | East Coast / Gulf Coast NOAA Coastal Flood Exposure Mapper | SLR, FEMA flood zones, Hurricane flood zones 2030, 2060, 2100 | Maps, composite scenarios, summary reports
Full Sea Level Rise and Coastal Flood Web Tools Comparison Matrix at (http://sealevel.climatecentral.org/matrix) that also shows state specific resources
Notes: DETAILED
Speaker Notes:
There are a number of regional or national sources that have already created sea level rise or sea level rise and storm surge flood inundation maps for coastal communities.

## Slide 75: Exposure: Inundation and Flooding Maps Creating Your Own Maps
Review existing tools, create new maps if necessary
Use best-available science: range of scenarios should reflect local guidance and polices, if available
Consider uncertainty and functional lifespan of assets to guide scenario selection
Promote consistency in scenarios and projections across city departments
Required Data: topography, shoreline protection surveys, water levels, asset locations
Image source: Creative Commons Flickr User ‘go_greener_oz’
Notes: DETAILED
Speaker Notes:
It is important to balance the most recent climate science with the availability of maps and models and the project’s resilience goals.
Project partners or a technical working group can assist in the selection of the climate scenarios, and can be excellent source of data and information that can be used to understand both existing and future climate impacts.
Use existing guidance or legislation to drive the scenario selection, and add or refine based on your system’s goals. Consider consistency among departments. Instead of creating individual scenarios on a department by department basis, consider creating a framework of scenarios for all departments to use going forward.
Avoid getting stuck in the selection of the “right” climate scenarios by taking a broad view that includes today as well as the near future (e.g., midcentury), where there is less uncertainty in the amount and timing of climate change. For the more distant future, where the amount and timing of climate change is more uncertain, choose the most plausible scenario and acknowledged it will be necessary to revisited the extent and timing of impacts in the future.
Covering uncertainty in more distant time horizons (e.g., select both intermediate and high end scenarios for 2100). Also consider the planning horizon or end lifespan expected for assets. If your asset is only expected to remain in operation for 50 more years, you don’t necessarily have to consider the end of century (e.g., 2100) scenario.
Image source: https://www.flickr.com/photos/go_greener_oz/

## Slide 76: Exposure: Inundation and Flooding Maps Mapping Methods
Bathtub
Simple GIS mapping exercise based on topography
All areas below flood elevation shown as flooded
Modified Bathtub
More detailed mapping exercise, accounts for hydrological connectivity
Commonly applied approach
Hydrodynamic Model
Accounts for duration of tide cycle, volume of storm
Time and cost intensive, but may provide more accurate results
Notes: DETAILED
Speaker Notes:
If these sources are not detailed enough for your community (or the scenario is not available), there are a number of paths available to create your own slr maps. The following slides provide some detail for creating new maps for your city/system.
The most commonly used methods are the bathtub mapping method, modified bathtub method, and creating a more sophisticated model. There are pros and cons to each method. A modified bathtub method is recommended as a providing enough detail without the data and time cost needed to create a model.

## Slide 77: Exposure: Riverine Flood Maps
FEMA NFIP Climate Change Study
  Estimates of changes in NFIP floodplain through 2100
  Factors climate change and population growth
  By 2100, the 1% annual change floodplain depth and extent is projected to increase, on average, by 45% across the nation
Notes: DETAILED
Speaker Notes:
We have mostly covered maps for coastal communities with sea level rise and coastal storms as the primary climate threat.
However, many communities are also impacted by flooding from riverine sources (i.e., rainfall runoff driven flooding). There are no nationally available datasets that illustrate the change in floodplain due to climate change (i.e., changing precipitation patterns and intensities). However, there are some sources that provide some useful information. One example is the FEMA NFIP Climate Change Study that shows the potential % increase in the FEMA Special Flood Hazard Area floodplain for the United States up to the year 2100 (based on climate and population change)

## Slide 78: Exposure: Inundation Maps Riverine
USGS Flood Inundation Mapper
  Visualize changes in river floodplain
  No climate change scenarios, but can identify thresholds of flooding
Notes: DETAILED
Speaker Notes:
There is a USGS web-viewer that visualizes the change in floodplain extent over a range of increasing river stage (levels). This is not specially tied to climate change, but can be used a proxy for understanding the thresholds where large-scale flooding can occur.

## Slide 79
Assessing Exposure Applicable Case Studies:
Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area
Notes: Assessing Exposure

## Slide 80
Assess Vulnerability Applicable Case Studies:
California State Route 37 Sea Level Rise Vulnerability Study and Adaptation
Notes: Assess Vulnerability

## Slide 81: Vulnerability Exercise – 1 of 2
Game Track: Do Vulnerability Assessment in workbook for Game of Floods
Exercise Track: No vulnerability exercise
Notes: Speaker Instructions:
For game-based track, have participants complete the Vulnerability Assessment in the Game of Floods Workbook using the instructions provided on the next slide.
Time: Allow 15 minutes
For the exercise-based track, trainers can delete this slide.

## Slide 82: Vulnerability Exercise – 2 of 2
Each team should use the Asset Cards, Asset Inventory Table, and the Game Board, to complete the Vulnerability Assessment Table.
The Total Vulnerability Score can be used to prioritize adaptation strategy selection.
Hint: Each team should decide how to assign the appropriate number of points for each asset, on a 3 point scale: Low (1 point), Medium (2 points), and High (3 points), for both Exposure and Sensitivity.
Notes: Speaker Instructions:
For game-based track, have participants complete the Vulnerability Assessment in the Game of Floods Workbook using the instructions provided on this slide.
Time: Allow 15 minutes
For the exercise-based track, trainers can delete this slide.
Game-based track:
Assign ratings Low (1 point), Medium (2 points), High (3 points) for the exposure and sensitivity of each identified asset.
Once exposure and sensitivity ratings are determined, calculate the overall vulnerability score (V = E + S).
Prioritize the assets based on vulnerability score.

## Slide 83: Assess Risk
How do we evaluate the likelihood and consequence of an impact?
Notes: Speaker Instructions:
The next set of slides provides an overview of how to assess risk of climate change hazards to assets.

## Slide 84: Process for Incorporating Climate Change into Project Planning - Step 4
1
2
3
6
5
4
Review Science
Inventory Assets and Operations
Assess Risk
Plan Adaptation
Implement Adaptation Measures
Monitor
Assess
Vulnerability
Stakeholder Engagement
Adaptive
Capacity & Thresholds
Physical Governance Information
Likelihood Consequence Prioritization
Exposure
Sensitivity
Adaptive
Capacity
Function Location Condition
Identify
climate scenarios
Adopt Construct
7
Notes: Speaker Notes:
The next step in the process for incorporating climate change into project planning is a Risk Assessment. Risk a function of likelihood and consequence and requires an understanding of both for a meaningful assessment. By combining both of these factors – likelihood and consequence of a given climate impact – asset managers can identify their most at-risk assets, which can help prioritize adaption actions.

## Slide 85: Defining Risk
Risk = Likelihood x Consequence
Likelihood = [Rare, Unlikely, Possible, Likely, Almost Certain]
Consequence = [Insignificant, Minor, Moderate, Major, Catastrophic]
Develop scoring for likelihood and consequence (1-5)
Notes: Speaker Notes:
Risk is defined as the product of likelihood and consequence. Likelihood of impact is rated using a relative rating system that ranges from rare events to events that are nearly certain to occur. Similarly, consequence is rated using a relative rating system that ranges from insignificant to catastrophic impacts. It is up to the professional conducting the risk assessment how to categorize and score likelihood and consequence. One way to do it is to assign ratings from 1 to 5 for each and use a matrix scoring system as shown in the next slide. A risk assessment helps differentiate the severity of impacts to different assets that may be exposed to the same climate hazard. For example, this small row boat and cruise ship may be equally likely to experience a storm event; however, the consequences to the row boat are much greater.

## Slide 86: Example Metrics for Likelihood
Likelihood | Descriptor | Recurrent Risks | Single Events
5 | Almost Certain | Several times per year | More likely than not – greater than 50%
4 | Likely | Once per year | As likely as not – 50/50
3 | Possible | Once per 5 years | Less likely than not but still possible – less than 50% but still quite high
2 | Unlikely | Once per 20 years | Unlikely but not negligible – low but greater than zero
1 | Rare | Once per 100 years | Negligible – Probability very small
Notes: Speaker Notes:
This slide provides one possible rating system for assigning likelihood scores for different events ranging from rare to almost certain.

## Slide 87: Calculating Consequence for Infrastructure and Services
Damage:
  What is the level of damage?
  Can the asset be repaired?
Disruption:
  Is there a disruption in service? How long? i.e., hours, days, weeks?
  Does the disruption threaten public health and safety?
Cost:
  What is the cost to repair or replace?
  Is there a cost associated with the disruption?
Notes: Speaker Notes:
This slide provides information on different ways to think about consequences of a climate impact to infrastructure and services in terms of damage to the asset, disruption of services, and cost to repair.

## Slide 88: Example Metrics for Consequence
Consequence | Descriptor | People | Infrastructure and Services
5 | Catastrophic | Multiple deaths and severe injuries | Loss of asset or critical service failure for extended period of time (>6 months)
4 | Major | Multiple deaths or severe injuries | Loss of asset function or major service failure for up to 1 month
3 | Moderate | Severe injuries | Moderate loss of asset function or moderate service failure for up to 1 week
2 | Minor | Major injury | Moderate service failure for up to 3 days
1 | Insignificant | Minor injury or near miss | Minor service interruption for <1 day
Notes: Speaker Notes:
This slide provides one possible rating system for assigning consequence scores for different events ranging from insignificant to catastrophic. Consequences can be considered in terms of impacts to human life or impacts to infrastructure and services, as described in the previous slide.

## Slide 89: Assessing Risk
Focus on most vulnerable and critical assets for risk evaluation
Risk ranges from negligible (for remote events with insignificant consequences) to extreme (for almost certain events with catastrophic consequences)
Low
Moderate
High
Notes: Speaker Notes:
This slide shows a risk matrix to identify a range of risk from negligible to extreme, depending on the likelihood of the impact and its consequence. A given asset may exhibit differing degrees of risk depending on the climate hazard being evaluated. For example, the likelihood of King Tide flooding of a roadway may be considered to be likely because it occurs on an annual basis (likelihood rating=4); however, the consequences may be negligible if the roadway is out of service for a few hours during high tide (consequence rating=1). Therefore, its risk rating would be green in the matrix and relatively low. In contrast, a hurricane may have high storm surge and waves that could wash out the road. While this event is relatively rare (likelihood rating=2), the consequence may be considered major because repair of the road may take several months (consequence rating=4). Therefore, its risk rating would be orange in the matrix (or moderate) because while the event would have major consequences for the roadway, hurricanes occur relatively infrequently.
Example guidance for taking action in response to risk ratings is provided below:
Extreme risk: issue requiring immediate action.
High risk: issue requiring detailed research and planning at senior management level.
Moderate risk: issue requiring change to design standards and maintenance of assets.
Low risk: issue requiring action through routine maintenance of assets.
Source: AS5334 Climate Change adaptation for Settlements and Infrastructure – A Risk Based Approach

## Slide 90
Assess Risk Applicable Case Studies:
Capital Regional District Coastal Sea Level Rise Risk Assessment
Notes: Assess Risk

## Slide 91: Risk Exercise (Optional) – 1 of 2
Game Track: Do Optional Risk (consequence) exercise in Game of Floods workbook
Exercise track:
Do Risk Assessment exercise in Participant Exercise Workbook
Notes: Speaker Instructions:
For game-based track, have participants complete the Optional Risk Assessment in the Game of Floods Workbook using the instructions provided on the next slide.
For the exercise-based track, have participants complete the Risk Assessment exercise in the Exercise Workbook.

## Slide 92: Risk Exercise (Optional) – 2 of 2
Think about the potential consequence of the sea level rise impact on each asset in terms of relative damage, disruption, and cost.
Complete the Optional Risk Assessment Table
Notes: Speaker Instructions:
For game-based track, have participants complete the Optional Risk Assessment in the Game of Floods Workbook using the instructions provided on this slide.
Time: Allow 15 minutes for this exercise
This slide can be deleted for the exercise based track.
Game-based track:
Describe consequences of climate change impacts on each asset in terms of damage, disruption, and overall relative cost.

## Slide 93: Adaptation Planning
How do we develop solutions to adapt to future climate change?
Notes: Speaker Instructions:
The next set of slides discusses both physical and non-structural adaptation strategies to cope with future climate conditions.

## Slide 94: Process for Incorporating Climate Change into Project Planning - Step 5
1
2
3
6
5
4
Review Science
Inventory Assets and Operations
Assess Risk
Plan Adaptation
Implement Adaptation Measures
Monitor
Assess
Vulnerability
Stakeholder Engagement
Adaptive
Capacity & Thresholds
Physical Governance Information
Likelihood Consequence Prioritization
Exposure
Sensitivity
Adaptive
Capacity
Function Location Condition
Identify
climate scenarios
Adopt Construct
7
Notes: Speaker Notes:
The next step in the process for incorporating climate change into project planning is the development of adaptation solutions to cope with future climate conditions. While this step represents the end of the adaptation planning process, it is only the beginning of the implementation process. Adaptation solutions span a range of disciplines and include both physical solutions (such as construction of new flood protection infrastructure) to governance and informational strategies (such as policy and code changes).

## Slide 95: Climate Change Adaptation
Physical Adaptation Strategies – Retreat | Accommodate | Protect
Non-structural Adaptation Strategies – Governance | Policy | Operational
Additional Resources for Adaptation:
Climate Adaptation Knowledge Exchange (www.cakex.org)
Georgetown Climate Center Adaptation Clearinghouse (http://www.adaptationclearinghouse.org)
Notes: Speaker Notes:
Physical or structural adaptation strategies refer to on-the-ground changes to infrastructure and can be categorized into three overarching categories – retreat, accommodate, and protect.
Retreat refers to the concept of moving vulnerable infrastructure out of harm’s way. Examples include realigning a roadway away from an eroding bluff or moving a beach restroom facility to higher ground. Or at a large scale, federal buy-out of neighborhoods damaged by flooding as was done in New York following Hurricane Sandy.
Accommodate refers to the concept of allowing some degree of flooding to occur for assets than may be less sensitive or lower risk to flooding. For example, a waterfront promenade may be designed in such as way that it is resilient to occasional temporary flooding during extreme high tides. During these times, the promenade could be temporarily closed and later re-opened once flood waters recede. Accommodating flooding is a viable solution particularly for water-dependent infrastructure, provided the infrastructure is designed in such as way to tolerate these conditions.
Protect refers to the concept of protecting critical infrastructure in place from flooding and erosion hazards. For example, building a seawall or levee to prevent flood waters from impacting the site.
Non-structural adaptation strategies can also be used to increase community resilience to future climate change hazards. These strategies typically are referred to as governance, policy, informational, or operational strategies. Examples include building code and policy updates, disaster response plans, floodplain ordinance updates, or city-wide adopting of sea level rise planning guidance which can improve community resilience to future climate change hazards incrementally over time as new projects are implemented.

## Slide 96: Adaptation Strategy Development
Prioritize Adaptation Needs based on vulnerability and risk assessment, timing of impact, criticality, and priority
Identify Strategies based on asset characteristics and climate hazard
Evaluate Strategies based on feasibility, cost, co-benefits, social equity, and other factors
Phase and Implement
Implement strategies and monitor
Notes: Speaker Notes:
Adaptation strategy development generally follows the four steps outlined in this slide.
The first step is to develop a prioritized list of adaptation needs. This prioritization is an outcome of the vulnerability and risk assessment and cities may decide to prioritize critical assets or services first. It is also important to consider the timing of impacts as adaptation actions for assets that will be impacted soonest may need to be prioritized.
The next step it to identify potential adaptation strategies for each asset. During this step, it can be helpful to review strategies implemented by other cities to see what strategies could potentially work for your asset. The suite of strategies to adapt an asset to future tidal inundation will be different than those to adapt an asset to extreme heat or rainfall flooding, for example. Similarly, the strategies that work in coastal North Carolina may be different than those applicable to an inland area along a riverine floodplain.
The next step is to evaluate the identified strategies to decide which ones will work best. This step is similar to an alternatives evaluation or feasibility assessment for a project, which is a process that you may already be familiar with. During this step, it is also important to consider all factors which contribute to selecting a strategy, including engineering feasibility, cost, co-benefits (such as coupling climate adaptation with ecosystem restoration), social equity (for example, impacts to public transit may disproportionately affect economically disadvantaged populations), and other factors.
The final step is to implement the adaptation strategies and monitor their effectiveness during changing climate conditions. Identifying thresholds for future adaptation actions and monitoring changes in environmental variables will alert cities when to initiate future phases of adaptation (for example, additional adaptation actions may occur after a region experiences 12” of sea level rise).

## Slide 97: Adaptation Strategies
Structural measures (relocation, raising structures, retrofit)
Non-structural measures (policy changes, operational modifications)
Asset-specific (focused on singular critical asset)
Regional (multiple assets and/or stakeholders)
Adaptation strategies
Notes: Speaker Notes:
In addition to differences between structural and non-structural adaptation measures, adaptation strategies can either be asset-specific or regional in nature. Regional strategies will require collaboration across multiple stakeholders and agencies and may be necessary particularly at political boundaries (for example, county or city lines) where an integrated solution is required. Examples of asset-scale and regional adaptation strategies are shown on the next slide.

## Slide 98: Planning Adaptation
Type of adaptation strategy
Scale
Operations, Management, and Policy
Region
Physical
Asset
Neighborhood
Sea Level Rise Policy
Building Code Update
Scale of protection
Notes: Speaker Notes:
Adaptation strategies and planning need to consider the scale of protection – for example, asset, neighborhood, or region. The type of strategy also needs to be considered – whether it is physical, governance, or operations and maintenance. It is also important to consider the timeframe for implementation of adaptation strategies and understand how vulnerabilities and risk change over time.
ANIMATED EXAMPLE: staged implementation using a flood-prone house as an example:
1- adding a flood barrier to house/asset is a short term solution
2 - In the medium term, it might be more feasible to construct a self closing flood barrier for the entire community
3 – In the long term, a more regional flood protection barrier may be required along with updates to policy and codes that improve the resilience of the entire housing stock over time.
Non-structural solutions can operate at a larger scale and provide a level of consistency to adaptation actions – for example, by standardizing the process by which capital improvement projects consider the effects of climate change or incorporating flood-proofing or green infrastructure standards for buildings located within existing or future floodplains.

## Slide 99
Adaptation Planning Applicable Case Studies:
California State Route 37 Sea Level Rise Vulnerability Study and Adaptation
Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area
Louisiana Coastal Master Plan
Notes: Adaptation Planning

## Slide 100: Developing Physical Adaptation Solutions
What physical changes can we make to adapt our infrastructure?
Notes: Speaker Instructions:
The next set of slides provide more examples of physical adaptation solutions within three broad categories: Protect | Accommodate | Retreat.

## Slide 101: Examples: Protect
Notes: Speaker Notes:
Flood protection strategies to adapt to future climate change are similar to strategies currently used to protect existing assets from current flooding issues, including tide gates, seawall, pumps, and levees. Many of the same challenges apply, including availability of land upon which to build these protective devices. When designing structural solutions for future conditions, it is common to design them in such a way that they can be adapted, or raised at some point in the future – for example, by adding more fill onto a levee or adding additional height to a seawall. When designing these structures, it is important to plan for these future modifications by incorporating a well-designed foundation that can support higher loading in the future or by providing a buffer adjacent to a levee to allow for placement of additional fill material when the crest elevation needs to be raised.
Source acknowledgement: Kristina Hill, UC Berkeley

## Slide 102: Examples: Accommodate
Non-structural: temporary road closure, rerouting traffic, alternate modes of transit, updated building codes and/or land use plans
Structural: Temporary flood barriers or sandbags, flood-proofing, improved drainage, raise electrical equipment, install pump stations, use more durable materials (e.g., epoxy-coated rebar, concrete mix specifications, sealant, etc.)
Source: FEMA (2013)
Source: americantrails.org
Source: precast.org
Notes: Speaker Notes:
In instances where relocation is not desired or possible, asset managers may be able to adapt infrastructure or operations to accommodate future climate hazards. For example, in the short-term, flooding caused by king tides or urban flooding caused by intense precipitation may happen relatively infrequently. In these cases, non-structural and structural solutions may be implemented to accommodate – or live with – temporary flooding. For example, roads could temporarily closed, traffic and transit could be rerouted, or flood-proofing of buildings could be mandated through an update to the building code or floodplain ordinance. Structural measures such as deployment of temporary flood barriers and sandbags or use of flood-resistant materials which are more durable to flooding could also reduce the exposure and sensitivity of assets to temporary flooding events.
Over the long-term, more substantial solutions may be required; however, in the short-term, these smaller-scale adaptation solutions could allow for the continued use and function of assets in the coming decades while more comprehensive adaptation strategies are developed.

## Slide 103: Examples: Managed Retreat
Notes: Speaker Notes:
Managed retreat is the process by which vulnerable (or damaged) infrastructure is removed from an existing or future hazard zone and relocated away from that hazard. In addition to reducing the vulnerability of assets by relocating them, managed retreat solutions can be coupled with habitat restoration projection which can both reduce flood hazards and provide ecosystem benefits and park areas for residents. There are small scale examples of managed retreat across the country – for example, Pacifica State Beach and Surfers Point (Ventura) in California and several projects in Cape Code, MA – as well as large scale examples such as the federal buy-out of neighborhoods impacted by flooding during Hurricane Sandy. Managed retreat does not have to implemented all at one time. A key component of managed retreat strategies is the identification of thresholds to trigger the demolition or relocation of assets in a phase approach. In some cases, assets can continue to be used in the near-time with the understanding that they will be removed over time.
Resources:
http://www.cakex.org/case-studies/restoration-and-managed-retreat-pacifica-state-beach
http://www.adaptationclearinghouse.org/resources/surfers-point-managed-shoreline-retreat-project.html
http://www.adaptationclearinghouse.org/resources/cape-cod-parking-lot-removal-and-relocation.html

## Slide 104: Evaluating Adaptation Solutions
How do we decide which adaptation solutions to implement?
Notes: Speaker Instructions:
The next set of slides will discuss different methods to evaluate adaptation solutions to guide in the selection of strategies that meet project and community goals and objectives.

## Slide 105: Evaluating Adaptation Solutions
  What is the availability of input data (e.g., asset data, socio-economic data, costs) to evaluate adaptation solutions?
  What is the availability of resources (e.g., time, expertise, money) to evaluate adaptation solutions?
  How well does the solution address the goals and objectives of adaptation?
  What is the past performance of the proposed solution?
  How able is the solution to accommodate future uncertainty in magnitude or timing of impacts?
Notes: OVERVIEW
Speaker Notes:
There are various methods to evaluate potential adaptation strategies once a core set of options has been identified. This slide lists some of the relevant questions that should be posed in the evaluation of potential adaptation solutions. Depending on available resources and expertise, differing degrees of evaluation may be possible. In the absence of rigorous evaluation of adaptation solutions, lessons learned and experience from other cities (or adaptation networks such as the Georgetown Adaptation Clearinghouse or Climate Adaptation Knowledge Exchange) can be great resources to learn from the experiences of others.
Adapted from: Handbook on Methods for Climate Change Impact Assessment and Adaptation Strategies (UNEP 1996)

## Slide 106: Evaluating Adaptation Solutions Key Steps
Identification of core strategies
Development of evaluation criteria
Selection of adaptation solutions for evaluation
Scoring of solutions against evaluation criteria
Ranking of adaptation solutions
Notes: Speaker Notes:
Because there are many different factors to consider when selecting adaptation strategies, it is important to evaluate strategies using objective methods of evaluation to the extent possible. This slide shows the high level steps in evaluating adaptation solutions from identifying core strategies and evaluation criteria, to selecting adaptation solutions for evaluation, to scoring those solutions against the selected criteria, to finally ranking the adaptation solutions for each asset.

## Slide 107: Potential Evaluation Criteria
Financial
Capital cost, operating and maintenance costs, lifespan, ability to minimize congestion
Governance / Administration
Ability to leverage jurisdictional collaboration, receive funding, or address legal issues
Stock photos source: pexels.com
Social
Ability to protect homes, jobs, amenities, and transit routes near communities of concern
Environmental
Ability to protect ecosystem value and functions and minimize GHG emissions or pollutants
Notes: Speaker Notes:
A variety of different factors should be considered when evaluating adaptation solutions. This slide shows four general categories for which evaluation criteria could be developed: financial, social, environmental, and governance/administration. Criteria can be developed within each category to provide metrics against which different adaptation solutions can be evaluated. Selected adaptation solutions should aim to balance all four categories, not necessarily select the solutions that score the highest. Methods of evaluation can be either qualitative or quantitative in nature.
Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area Pilot Project (MTC 2014)

## Slide 108: Qualitative Assessment of Strategies
Qualitative ranking system to evaluate strategies
Evaluate trade-offs between categories and select balanced alternatives
Develop criteria within Financial, Social, Environmental, and Administration categories
Scoring should be supplemented by local knowledge and experience
Levee
Breakwater
Notes: DETAILED
Speaker Notes:
This slide shows one example of a qualitative method to evaluate the trade-offs associated with different adaptation strategies, using the categories discussed on the previous slide – Financial, Social, Environmental, and Governance/Administration. Evaluation criteria within each category are developed and each strategy is rated relative to one another. Ratings for each criteria range from “significantly positive” to “neutral” to “significantly negative” and ratings are organized graphically on the wheel diagram. This example shows an evaluation of two coastal protection strategies – a levee and a breakwater in San Francisco Bay. For Financial Criteria “F2” (Annual operating and maintenance costs), both strategies scored poorly, but both scored well on Financial Criteria “F3” (lifespan).
Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area Pilot Project (MTC 2014)

## Slide 109: Types of Evaluations
Method | Level or Precision | Inputs Needed | Resource Requirements
Forecasting by analogy | Low | Historical data/contemporary accounts | Moderate
Screening | Low | Expertise knowledge for yes/no decisions | Low
Decision matrix | Moderate | Expertise to establish ranking, ability to estimate costs | Moderate
Benefit-cost analysis | High | Data intensive | High
Cost-effectiveness analysis | Useful when benefits or costs are fixed | Moderately data intensive | High
Implementation analysis | Assume benefits are positive and comparable among measures | Expertise to estimate requirements for overcoming barriers | Low
Source: Handbook on Methods for Climate Change Impact Assessment and Adaptation Strategies (UNEP 1996)
Notes: DETAILED
Speaker Notes:
Adapted from: Handbook on Methods for Climate Change Impact Assessment and Adaptation Strategies (UNEP 1996)
Here are details on several additional types of evaluations that can be used to better understand the impact that implementing a particular adaptation strategy may make:
Forecasting by analogy:
Empirical investigations of adaptation to present-day climate variability or to climate events in the past provide insights into the process of adaptation and the conditions needed for its successful promotion. Forecasting by analogy looks at events that have had a similar effect in the recent past to the likely impact of future events associated with climate change.
Screening:
This approach relies heavily on expert judgement. Expert judgement can be used to develop a preliminary evaluation of various adaptation measures or to identify measures for further research. In addition, approaches that rely on expert judgement are often useful for involving decision makers and key stakeholders and can be used to build consensus. However, it is important to recognize that in applying these approaches it is possible to tailor a case to make a certain strategy appear to be better than others. Therefore, justification of each decision that relies on expert judgement should be provided.
Decision matrix:
This approach uses a decision matrix to analyze the cost-effectiveness of adaptation options by comparing costs measured in dollars with benefits measured in a common metric, but not necessarily monetary units.3 This approach is useful when many important aspects of a decision cannot be easily monetized.
Benefit-cost analysis:
Unlike cost-effectiveness analysis and multi-criteria assessment, benefit-cost analysis can be used to determine whether an individual adaptation response is economically justified (i.e., are its benefits greater than its costs?) The other evaluations can be used to rank responses but not to determine whether they should be undertaken at all. A benefit-cost analysis involves essentially two steps: identifying and screening benefits and costs to be included in the analysis, and converting them to monetary units when possible. No economic analysis is able to account for every benefit and cost, but including all important benefits and costs is key to a valid analysis.
Cost-effectiveness analysis:
Cost-effectiveness analysis is a variation of cost-benefit analysis in which either benefits or costs are fixed. This method is applicable when it is difficult to quantify and monetize benefits. In such cases, it may be possible to compare adaptation measures by determining their cost differences for achieving a fixed level of effectiveness.
Implementation analysis:
Relies on expert judgement and allows for consideration of multiple criteria is implementation analysis. Rather than evaluating the relative benefits from different adaptation measures, this method focuses on identifying the least costly measure (in terms of money, time, political capital, etc..). This approach is useful when it can be assumed that the benefits of different adaptation measures will be comparable. In applying this method, the analyst identifies any implementation barriers and evaluates how difficult or easy it will be to overcome these barriers. A matrix can be used to identify barriers, actions to overcome the barriers, what time and financial resources are required, and the degree of difficulty (i.e., a summary of the other criteria) in overcoming the barriers. A three-point rating system can be used in which one X represents the barrier easiest to overcome and three Xs represent those most difficult to overcome.

## Slide 110: Evaluating Adaptation Solutions Benefit-Costs Analysis
  Benefits:
  Help weigh potential adaptation strategies in terms of costs and benefits
  Facilitate the evaluation of longer-term adaptation strategies against other types of investments (e.g., short-term immediate needs projects).
  Direct comparison of benefit–cost ratios, can help align support for adaptation projects amid immediately pressing agency needs.
  Free resource: FHWA Benefit Cost Analysis (BCA) tool can be used at the project level.
    Allows consideration of design, timing, and strategic alternatives based on array of benefit-cost measures.
Notes: DETAILED
Speaker Notes:
Benefit-costs analysis is a method of alternatives analysis that helps weigh potential adaptation strategies in terms of their costs and benefits.

## Slide 111: Evaluating Adaptation Solutions Triple Bottom Line Assessment
  Considers economic, environmental, and social consequences
  A broader range of impacts (besides economic costs / benefits) are considered for each bottom line
  Will not answer which option is “best”, but can organize information along the three bottom lines to better inform decision-makers
Notes: DETAILED
Speaker Notes:
Triple Bottom Line Analysis provides a full accounting of the financial, social, and environmental consequences of investments or policies.
Often “TBL” analysis is used to identify the best alternative and to report to stakeholders on the public outcomes of a given investment.

## Slide 112
Evaluating Adaptation Solutions Applicable Case Studies:
California State Route 37 Sea Level Rise Vulnerability Study and Adaptation
Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area
City of Toronto – Preparing for Climate Change and Wet Weather Flow Master Plan
New York City Green Infrastructure Plan
Chicago Green Infrastructure
Notes: Evaluating Adaptation Solutions

## Slide 113: Integrating Climate Change into Planning & Operations
How do we mainstream climate change preparedness?
Notes: Speaker Instructions:
The next set of slides discusses approaches to mainstream (or operationalize) climate change preparedness into city operations.

## Slide 114: Mainstreaming Climate Change Adaptation
Mainstream Adaptation
Systematically incorporate climate change planning
Consider climate change a fundamental component of project design
Establish
Overarching Policy
Adopt formal policy statement on climate change
Pursue Adaptation Funding
Prioritize funding for climate change adaptation
Pursue grants, bonds, insurance, disaster aid, fees, taxes, etc.
Integrate into
City Programs
Integrate into planning, capital development, operations, maintenance, and administration
Convey importance to state and federal policy makers
Notes: Speaker Notes:
This slide presents the four primary steps for integrating climate change preparedness into planning and operations:
- Mainstream climate change adaptation refers to the systematic incorporation of climate change considerations in planning, design, and operations of a city and all its processes
- Establishing a climate change policy can be accomplished through adoption of a formal policy statement recognizing climate change as a hazard that needs to be planned for at a citywide level.
- Integrating climate change into agency programs can be accomplished through the development and adoption of planning guidance or checklists for projects to ensure that all projects go through the same process to consider the effects of climate change on project success.
- Funding prioritization which looks at ways to identify and secure funding for climate change adaptation through various means.
The next four slides present specific points on how to integrate climate change into agency programs. These are divided by sector/department:
Planning;
Capital development;
Operations and maintenance; and
Administration.
Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area Pilot Project (MTC 2014)

## Slide 115: Mainstreaming Climate Change Adaptation: Planning
  Convene and coordinate climate adaptation-focused agency groups
  Work with partners to generate local knowledge and data on climate projections and impacts
  Formulate climate-focused statements on the department’s vision, values, mission, goals, performance indicators, and implementation
  Integrate climate change considerations in processes to identify and prioritize community needs
Notes: Speaker Notes:
Integrating climate change into planning
This slide focuses on the Planning Division.
Key Responsibilities of the Planning Division – Convene and coordinate activities among various departments in City Government. Contribute to knowledge generation (e.g., identifying future housing and employment needs, etc..). Develop and update policies/plans that establish a vision for the (transportation, stormwater, wastewater) system in the future. Identify and prioritize projects that address critical system needs in preparation for project development.
Specific contributions to climate change preparedness include:
Convening – can provide support and offer technical advice to agency-wide coordinating body
Coordinating – Forging new connections to partners knowledgeable in climate change adaptation such as research institutes, peer agencies already addressing climate change
Strategic Visioning – Integrate climate change preparedness into the agency’s long-term vision and strategic development
Needs Identification – Integrate climate risk into needs identification and prioritization
Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area Pilot Project (MTC 2014)

## Slide 116: Mainstreaming Climate Change Adaptation: Capital Planning
  Consider climate risk when developing and prioritizing capital improvement projects
  Incorporate climate risk and resilience in project design
  Update design guidelines, standards, and specifications to promote climate resilience
  Train engineers to select appropriate design criteria that consider climate impacts
  Adjust permitting requirements to incentivize climate resilience
  Incorporate climate risks into asset management and renewal cycles
Notes: Speaker Notes:
Integrating climate change into capital planning
This slide focuses on the Capital Planning Division.
Key Responsibilities of the Capital Planning Division – Prioritize projects that require significant capital investment, contribute to project scoping, contribute to drafting design guidelines and standards for infrastructure projects, project engineering and construction, permitting of infrastructure projects, and routine asset management.
Specific contributions to climate change preparedness by the capital planning division could include:
Integrate climate risk into project prioritization – particularly those requiring significant capital investments.
Consideration of climate change in project development and scoping could identify fundamental design challenges and promote consideration of adaptation strategies
Design guidelines, standards, and specifications can be updated to reflect the agency’s risk tolerance and guide project design
During the permitting process, a proactive dialogue with partner environmental agencies could support the identification of solutions that protect the environment (and adjacent landowners) while turning asset renewal activities, and even disasters, into opportunities to enhance the resilience of otherwise vulnerable facilities. Identification of potential projects in hazard mitigation plans is one way to secure funding for these types of projects.
Incorporate projected future risks into asset management regimes today so that the asset renewal cycle (including capital investments as well as operations and maintenance) and specific treatments can be adjusted to maximize the agency’s investment dollars.
Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area Pilot Project (MTC 2014)

## Slide 117: Mainstreaming Climate Change Adaptation: Operations and Maintenance
  Consider climate and extreme weather changes in planning for future emergencies (for example, staffing)
  Coordinate with other city departments to develop robust responses to climate-related emergencies
  Obtain feedback from maintenance staff about the success, failure, and cost of maintenance for implemented solutions
  Document extreme weather frequencies and trends to inform decisions regarding purchasing of materials and equipment
Notes: Speaker Notes:
Integrating climate change into Operations and Maintenance
This slide focuses on the Operations and Maintenance Division.
Key Responsibilities of the O&M Division – The O&M has specific responsibilities in times of natural disasters that are to do with emergency operations and evacuation. O&M also has coordination responsibilities with other departments involving emergency preparedness. Maintenance personnel have are responsible for maintaining the physical and functional condition of infrastructure. Finally, O&M is also in charge of maintaining an adequate stock of maintenance and emergency preparedness/response material and equipment.
Specific contributions to climate change preparedness by the O&M division could include: obtaining climate projections data to inform tweaks to emergency response and evacuation procedures; educating other city departments about emergency response procedures that account for climate impacts, tapping into the knowledge of maintenance personnel about the current conditions of physical infrastructure, and using projections data to inform purchasing decisions.
Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area Pilot Project (MTC 2014)

## Slide 118: Mainstreaming Climate Change Adaptation: Administration
  Actively back climate adaptation-focused policy, priorities, and partnerships
  Support adaptation dialogue with partner agencies and legislative bodies
  Support stakeholder outreach to highlight need to address climate change
  Support the development of future budget needs to address anticipated changes in climate
  Leverage the cross-departmental coordination of sustainability department to address climate resilience
Notes: Speaker Notes:
Integrating climate change into General Administration
This slide focuses on the City Administration Division. Responsibilities fall within the Executive Management, Government Relations, Public/Media Relations, Finance, and Sustainability roles.
Key Responsibilities of the Administration Division – The administration division is responsible for maintaining city relationships with other public agencies as well as the general public. This division also influences the City’s general fund, and often takes on sustainability-related projects, particularly those focusing on greenhouse gas reduction.
Specific contributions to climate change preparedness by the Administration division could include: supporting adaptation planning dialogue with regional, state, and federal agencies; communicating efforts on local and regional climate adaptation planning with the media, providing general direction on how city general funds can be used or leveraged for adaptation planning, and how synergies can be explored between the city’s sustainability planning efforts and adaptation planning.
Resource: Climate Change and Extreme Weather Adaptation Options for Transportation Assets in the Bay Area Pilot Project (MTC 2014)

## Slide 119: Examples of Planning Documents that can Incorporate Climate Change Considerations
City General and Specific Plans
  Land use and Transportation element
  Flood hazard mitigation element
Municipal building codes/Green building ordinances
  Measures for flood proofing
  Required minimum elevations
Floodplain ordinances
  Regulate development in floodplains to accommodate future conditions
  Required insurance for structures in floodplains
Stormwater management plans
  Runoff control guidelines for private properties
  Add larger catch basins
  Allow for green infrastructure to reduce runoff
Notes: DETAILED
Speaker Notes:
This slide provides specific examples of where to adopt climate change policies and promote resilience within city operations, including updates to building codes, floodplain ordinances, stormwater management plans, or transition to renewable energy.

## Slide 120: Examples of City Plans and Documents that can Incorporate Climate Change Considerations
Storm Drainage Design Standards
  Measures for flood proofing
  Required minimum elevations
County Flood Control District Manuals
  Hydrology and Hydraulics Manuals (update to include future conditions analysis methods)
Storm Drainage Design Standards
  Design criteria, standards, policies, and procedures for storm drainage improvements
Strategic Plans/Master Plan
  High level documents outlining future priorities
Infrastructure Design Criteria Manuals
  Standardized guidance for infrastructure design projects
Notes: DETAILED
Speaker Notes:
This slide provides specific examples of where to adopt climate change policies and promote resilience within city operations, including updates to building codes, floodplain ordinances, stormwater management plans, or transition to renewable energy.

## Slide 121: Adaptation Plan Exercise – 1 of 2
Game Track: Do Adaptation Plan exercise in Game of Floods workbook
Exercise track: Do Project Resilience Review in Participant Exercise Workbook (and on subsequent slides)
Notes: Speaker Instructions:
For game-based track, have participants complete the Adaptation Plan in the Game of Floods Participant Workbook.
For exercise-based track, have participants complete the Project Resilience Review exercise on subsequent slides.

## Slide 122: Adaptation Plan Exercise – 2 of 2
Each team should report out on their Adaptation Plan
If there was one thing you wanted to do, but could not afford, what was it?
Notes: Speaker Instructions:
For game-based track, have participants complete the Adaptation Plan in the Game of Floods Participant Workbook.
This slide can be deleted for the exercise-based track.
Game-based track:
Review potential adaptation options and associated costs.
Teams will strategize how to protect assets with allotted funding.
All team members should record results in their own workbook.
Teams will also consider additional 2 questions in workbook:
  -Think about outreach and engaging the community, what activities would you need to complete as you implement your Plan?
  -If there is one more thing you wanted to do to increase the resiliency of the town to climate change, but you could not afford, what would it be and why?

## Slide 123: Project Resilience Review – 1 of 2
Review the project example provided by the trainer
Review details of future exposure to one or more flooding scenarios
Annotate project drawing/aerial, identifying opportunities and constraints and potential adaptation solutions
Address questions on following slide
Notes: Speaker Instructions:
For exercise-based track, have participants complete the Project Resilience Review on this slide and the next.
This slide can be deleted for the game-based track.

## Slide 124: Project Resilience Review – 2 of 2
Which climate change stressors affect the project?
What constraints does the site have?
What adaptation strategies might be possible?
What are the opportunities for social, equity, economic, and environmental benefits to the City?
What are the short, medium and long term benefits?
Are there any potential risks or negative consequences?
How can the project highlight interdependencies between systems or sectors?
What stakeholders should be involved in the project?
In summary, how could it contribute overall to the resilience of City?
Notes: Speaker Instructions:
For exercise-based track, have participants complete the Project Resilience Review on this slide and the previous.
This slide can be deleted for the game-based track.

## Slide 125
Integrating Climate Change into Planning & Operations Applicable Case Studies:
Vancouver Flood Resilience and Adaptation
Fort Lauderdale Mainstreaming Resiliency
Baltimore Amendment of Floodplain Code
Climate Change Preparedness and Resiliency Checklist, City of Boston
San Francisco Capital Planning Guidance
Miami Beach Proposed Code Modifications
MTC Mainstreaming Climate Change Risk
Baltimore Capital Improvement Program
Port of Long Beach, Addressing Climate Change
Notes: Integrating Climate Change into Planning & Operations

## Slide 126: Wrap-Up What next?

## Slide 127: Process for Incorporating Climate Change into Project Planning – Next Steps
1
2
3
6
5
4
Review Science
Inventory Assets and Operations
Assess Risk
Plan Adaptation
Implement Adaptation Measures
Monitor
Assess
Vulnerability
Stakeholder Engagement
Adaptive
Capacity & Thresholds
Physical Governance Information
Likelihood Consequence Prioritization
Exposure
Sensitivity
Adaptive
Capacity
Function Location Condition
Identify
climate scenarios
Adopt Construct
7
Notes: Speaker Notes:
Following completion of an adaptation plan for an given asset or set of assets, it is time to implement adaptation measures. This involves constructing the selected physical adaptation strategies or adopting or implementing selected governance strategies. As discussed previously, it is important to continue to monitor changing environmental conditions to identify thresholds at which point phased strategies may be implemented. Thresholds are especially important to identify to assets design with adaptive capacity, where structural modifications are planned at some point in the future or for managed retreat projects where assets are removed and relocated according to a predetermined plan triggered by exceedance of future thresholds.

## Slide 128: Incorporating climate change into project planning and design (Optional) What ideas do you have to incorporate climate change considerations in your day-to-day work? What other staff or departments can you coordinate with?
Notes: [OPTIONAL SLIDE]
Speaker notes:
Based on what you’ve learned today, what ideas do you have to incorporate climate change considerations in your day-to-day work?
This is an optional slide that can be used to facilitate a brief discussion among staff to wrap up the training and promote thinking about next steps.